## Slide 1: OPACITY QUALITY ASSURANCE, LEGAL PERSPECTIVE AND METHODS
Bob Scott

## Slide 2
OPACITY
QUALITY ASSURANCE AND LEGAL PERSPECTIVE
DOCS II - Digital Opacity Compliance System II
FORMS & DOCUMENTATION
METHOD 9 - (METHODS 203A, B, C)
METHOD 22 - Subpart Dc Boilers
SLIDE PRESENTATION
SUBPART OOO
SUPART UU
AIR CURTAIN DESTRUCTORS

## Slide 4
Comparison of Method 9 and 22

## Slide 5: Comparison of Method 9 and 22
 | METHOD 9 | METHOD 22
Distance From Source | No distance is specified, but the observer must have a clear view of the emissions. | From 15 feet to 0.25 mile.
Viewing Angle | Observer views the plume from a position that minimizes the line of slight through the plume to minimize positive bias. | Observer simply observes the plume.
Light Source | The sun is implied as the light source and it is required to be at the observer’s back. | Light sources other than the sun are acceptable but must be documented. The light must be at least 100 lux. But, it is not required to be at the observer’s back
Viewing Times | Momentary observation every 15 seconds for a period determined by the standard. Each observation is recorded. | Continuous viewing with observer rest breaks every 15 to 20 minutes. The observer times the emissions with a stopwatch and records the duration of emissions.

## Slide 6
Digital Opacity Compliance System II (DOCS II)
DOCS II aligns with most aspects of Method 9:
  Smoke school certification
  Certification records
DOCS II certified to ASTM 7520-09 method
DOCS II can be applied as an equivalent to Method 9
DOCS II can be used as a field data acquisition support tool in conjunction with traditional human observations
DOCS II sets a new standard for Credible Evidence in the Visible Emissions measurement.
(USAF) Field validation study:
www.serdp.org/content/download/5888/80446/file/SI-0119-FR.pdf

## Slide 7
Handheld Real Time Climatic Sensor
Handheld Data Collection Device for DOCS II Application
  One Device Collects all Required Data
  Error-Free Automated Data Collection
Integrated Weather Meter, GPS, Rangefinder, & Camera
  Measures all Required Report Data: Weather Conditions, Wind Speed, Wind Direction, Temperature & Humidity
  GPS Position Location, Sun Position, & Time
  Distance to Target Missions Source
  Digital Images of Visual Emissions & Source
Creates Digital Reports in the Selected Format
Only Works as an Upgrade with PC based DOCS II

## Slide 9: LEGAL ASPECTS OF VISIBLE EMISSIONS

## Slide 10: LEGAL ASPECTS
WHO IS AN EXPERT?
Has Special Knowledge or Talent (i.e.., SMOKE SCHOOL)
May Testify As To His Opinions or Conclusions Based Upon Training and Experience.

## Slide 11
BECOMING AN EXPERT WITNESS
ATTENDING a Course Such as this One.
Successfully PASSING a Test.
Successfully COMPLETING the Required Observations with the Required Proficiency.
LEGAL ASPECTS

## Slide 12
ATTEND LECTURE, PASS TEST, PASS FIELD WORK...
...AND YOU’RE
AN EXPERT!!!
LEGAL ASPECTS

## Slide 13
If there is a question of the witness’ qualifications, it will reflect on the WEIGHT that is given his testimony, NOT on admissibility of his testimony.
EXPERT WITNESS’ COMPETENCY
LEGAL ASPECTS

## Slide 14
IMPORTANT TO LIMIT YOUR OPINIONS TO YOUR AREA OF EXPERTISE.
AN EXPERT (FOR OUR PURPOSES) MAY NOT TESTIFY AS TO CONCLUSIONS OF LAW (i.e.., WHETHER OR NOT AN OBSERVATION INDICATES A VIOLATION OF A STATUTE OR REGULATION)
HOWEVER, ONE COULD TESTIFY THAT AN OBSERVATION INDICATES AN OPACITY OF 10%, 20%, 50%, etc....
LEGAL ASPECTS
On the Witness Stand

## Slide 15
May Not Be Used as Evidence of Shade of the Plume or background.
Useful To Depict Distances and Locations (Position).
Have Complete Record of the Chain of Custody Film and Photos.
Make Sure You Know Camera and Film Data and Settings.
Make Sure You Know Which Facility Processes Your Have Photographed.
LEGAL ASPECTS
Filming

## Slide 16
LEGAL ASPECTS
      VIOLATIONS
$100 PER day
PER Violation
$25,000 PER day
PER Violation

## Slide 17
UP TO $250,000
IN ANY ONE ORDER
LEGAL ASPECTS

## Slide 18
UP TO 1 YEAR IN COUNTY JAIL
LEGAL ASPECTS

## Slide 19
PLUME BEHAVIOR
Attached
Detached
Acid

## Slide 20: Attached steam plume
Read Here

## Slide 21: Detached steam plume
In rare cases, it may be necessary to make readings at the point of steam dissipation if the plume is more opaque at that point.
Read Here
(preferred)
Read Here
(Preferred)
Or Read Here
Point of Steam Dissipation

## Slide 22: Acid plume
Below is a plume from a sulfuric acid plant with a detached steam plume. Plume is clear at the stack exit. Secondary acid mist is formed in area of steam condensation.
Read Here
Read Here
Point of Steam Dissipation

## Slide 23: Slant Angle

## Slide 24: L Prime

## Slide 25: Slant angle accuracy
Variation of observation angle and path length with distance from an elevated source.

## Slide 26: Typical Plumes

## Slide 27: Plume Graphics

## Slide 28: Lofting
LOFTING
Notes: FUMIGATING PLUME

## Slide 29: Looping 2

## Slide 30: Coning

## Slide 31: Coning detached
Coning

## Slide 32: Detached Plume 3

## Slide 33: Attached Steam Plume

## Slide 34: Detached Steam Plume 4

## Slide 35: Coning 3

## Slide 36: Fanning

## Slide 39: Steel Production

## Slide 41: Interference

## Slide 42: Contrast

## Slide 43: Contrast 3

## Slide 44
White Smoke

## Slide 45: Wood Dryer White

## Slide 46: Wood Dryer Black

## Slide 47: 4 stacks
Interference

## Slide 49: Interference

## Slide 50: Meteorological Instruments

## Slide 51
Hygrometer
Measures Relative Humidity

## Slide 52
Thermometer
Measures Temperature

## Slide 53
Anemometer
Measures Wind Speed

## Slide 54: METHOD 9
METHOD 9 INCLUDES:
Procedures for Training and Certification of Observers
Procedures to Be Used In the Field for Determination of Plume Opacity

## Slide 56
SIX MINUTE AVERAGE
  Shall be determined by calculating the arithmetic mean of twenty-four (24) consecutive opacity observations
  Taken at intervals of fifteen seconds
Field Procedures

## Slide 57
Method 203A
VARIABLE AVERAGING TIME (e.g. TWO MINUTE AVERAGING TIME)
Shall be determined by calculating the arithmetic mean of eight (8)consecutive opacity observations
Taken at intervals of fifteen seconds
Method 203B
SIX MINUTE AVERAGE
Shall be determined by calculating the arithmetic mean of twenty-four (24)consecutive opacity observations
Taken at intervals of fifteen seconds
Allows for time exceptions – (e.g., allowing exceedances of 20 percent opacity for 3 minutes in 1 hour.)
Field Procedures - Alternates

## Slide 58
Field Procedures - Alternates
Method 203C
SIX MINUTE AVERAGE
Shall be determined by calculating the arithmetic mean of Seventy-two (72) consecutive opacity observations
Taken at intervals of five seconds
M 203A data-reduction procedures which provide for averaging times other than 6 minutes. M203B. A time-exception regulation means any regulation that allows predefined periods of opacity above the otherwise applicable opacity limit (e.g., allowing exceedances of 20 percent opacity for 3 minutes in 1 hour.) M203C Allows for 5-second reading intervals and the data-reduction procedures, which have been modified for instantaneous limitation regulation

## Slide 60
5 10 5 20 5 5 5 5
5 5 5 5 10 5 5 5
10 25 5 5 10 5 10 5
15 10 10 5 5 5 5 5
5 5 10 5 10 15 20 5
5 5 5 5 5 5 5 5
5 10 25 10 5 5 5 5
5 5 10 5 5 5 5 5
15 25 45 10 20 5 10 5
5 10 5 10 5 10 5 10
20 30 40 40 5 10 5 10
15 10 5 10 10 5 10 5
5 15 10 5 10 15 20 5
5 10 5 5 10 5 5 5
5 0 0 0 5 5 5 5
5 5 5 5 5 5 5 5
0 5 5 0 5 5 5 5
5 5 5 5 5 5 5 5

## Slide 61
5 10 5 20 5 5 5 5
5 5 5 5 10 5 5 5
10 25 5 5 10 5 10 5
15 10 10 5 5 5 5 5
5 5 10 5 10 15 20 5
5 5 5 5 5 5 5 5
5 10 25 10 5 5 5 5
5 5 10 5 5 5 5 5
15 25 45 10 20 5 10 5
5 10 5 10 5 10 5 10
20 30 40 40 5 10 5 10
15 10 5 10 10 5 10 5
5 15 10 5 10 15 20 5
5 10 5 5 10 5 5 5
5 0 0 0 5 5 5 5
5 5 5 5 5 5 5 5
0 5 5 0 5 5 5 5
5 5 5 5 5 5 5 5

## Slide 62
5 10 5 20 5 5 5 5
5 5 5 5 10 5 5 5
10 25 5 5 10 5 10 5
15 10 10 5 5 5 5 5
5 5 10 5 10 15 20 5
5 5 5 5 5 5 5 5
5 10 25 10 5 5 5 5
5 5 10 5 5 5 5 5
15 25 45 10 20 5 10 5
5 10 5 10 5 10 5 10
20 30 40 40 5 10 5 10
15 10 5 10 10 5 10 5
5 15 10 5 10 15 20 5
5 10 5 5 10 5 5 5
5 0 0 0 5 5 5 5
5 5 5 5 5 5 5 5
0 5 5 0 5 5 5 5
5 5 5 5 5 5 5 5

## Slide 64
METHOD 22
TWO TIME PIECES NEEDED
1. Observation period
2. Totalize emissions
1 2

## Slide 65: HYBRID M9-M22

## Slide 66
Flare Plume

## Slide 67
High Flare Opacity

## Slide 68: M22 Indoor Form

## Slide 69: M22 Outdoor Form

## Slide 70: Roofing Plant Graphic

## Slide 71: M22 – 3

## Slide 72: M22 - 2
Duplicate? Other pics underneath.

## Slide 73: Quarry graphic

## Slide 74: Wet Suppression System

## Slide 75: Rock Quarry

## Slide 76: Quarry Safety

## Slide 77: Quarry Positioning

## Slide 78: Quarry Positioning 1

## Slide 79: Quarry Primary

## Slide 80: Quarry Road Wetting

## Slide 81: Quarry Wind-Stockpile

## Slide 82: HOW DO I PASS ?
HOW TO AVOID FAILING

## Slide 83: <3 Increments 3>
5
10
15
20
25
30
35
40
45
X

## Slide 84: Transmissometer

## Slide 85: Contrast 2

## Slide 86: White Plume

## Slide 87: Black Plume

## Slide 88
BLACK SMOKE

## Slide 89: WIND SPEED
Effects plume dispersion.
  High Winds - Greater dispersion.
  Low Winds - Less dispersion.
Effects plume rise.