## Slide 1: Maintenance Plan Development Results

## Slide 2
Nonattainment Area
Overview
As of the end of 2015, the Atlanta Region is meeting the 2008 Ozone Standard
A Maintenance Plan is required to show how the region will stay in attainment in the future
Maintenance Plans require the development of new emission budgets, including motor vehicle budgets (MVEB)
The new 15-county budgets would replace all existing 20-county ozone budgets for the Atlanta region
ARC and GA EPD worked together to test new MVEBs by projecting future transportation needs out to 2050 and developing the data in this report

## Slide 3
Budget Timeline
2014
2050
2030
Budget Period 1
Budget Period 2
Attainment Year
Maintenance Plan Horizon Year
Likely Planning Horizon Year
Previously, the region was meeting 2 sets of 20-county budgets – Reasonable Further Progress SIP budgets to 2024 and 2012 Maintenance Plan SIP Budgets in 2024 and later years
Budget 1 set based on 2014 model runs
Budget 2 set based on 2030 model runs

## Slide 4
Ozone Precursor | 2014 Tons/Day | 2030 Tons/Day | 2050 Tons/Day
NOx | 170.15 | 37.57 | 29.40
VOC | 81.76 | 32.67 | 25.70
Results of Emissions Model Runs
Chart: Emissions Analysis Year
| 2014 | 2030 | 2050
NOx | 171.1275 | 37.6409 | 29.4046
VOC | 81.8273 | 32.6693 | 25.7041

## Slide 5
Emissions Curve & Safety Margins
2014
2050
Budget Period 1
Budget Period 2
Attainment Year
Maintenance Plan Horizon Year
Likely Planning Horizon Year
MOVES2010
2010 Maintenance Plan
MOVES2014a
2015 Maintenance Plan
MVEB A
2050 emissions > MVEB A =
Blown MVEB
MVEB B
2050 emissions < MVEB B
=
Safe MVEB
Minimum Safety Margin

## Slide 6
Safety Margins Background
MVEBs can last for a long time; Safety Margins provide a buffer from uncertainty in planning and modeling changes. Safety Margins are widely used across the nation.
In 2010, ARC determined the allocation of Safety Margins for use in MVEBs. These MVEBs included safety margins of between 25 – 50%.
This work was repeated in 2015 as a minimal safety margin in addition to more work outlined below to find maximum bounds.

## Slide 7
Safety Margins Methodology
2010 Method Test
  10% increase in VMT
  1 million more population
  2 years older fleet
Upper Method
  VMT was adjusted to the next model year’s values +10%
    2030  2050 +10%
  Population/Starts was adjusted to the next model year’s values
  2 year older fleet
2014
2050
2030
2050 Data
VMT
Population
SE Data
Starts

## Slide 8
Safety Margin Input Changes Compared to Baseline
Safety Margin 2010 Method Tests | Change of 2030 Safety Margin Inputs (2010 Method Test) | Change of 2030 Safety Margin Inputs (Upper Method Test)
Annual VMT | 10% | ~ 35%
Vehicle Population | 10% | ~ 30%
Starts | 10% | ~ 25%
Age Distribution | + 2 years | + 2 years

## Slide 9
Safety Margin Emission Results
Ozone Precursor | 2030 Base (tons/day) | 2030 Safety Margins (2010 Method) | 2030 Safety Margin (Upper Method)
NOx | 37.57 | 47.95 (+27%) | 57.76 (+54%)
VOC | 32.67 | 43.74 (+34%) | 51.88 (+59%)

## Slide 10
Final Budgets / Safety Margins Requested
For 2014 Budgets
  No Safety Margins permitted since it’s the baseline attainment year
For 2030 Budgets
  Since there is more uncertainty in modeling further out years, and the magnitude of the emissions changes are smaller, ARC requests that the budgets be set towards the higher limit to match the Upper Method Test
Ozone Precursor | 2014 Modeled Tons/Day (MVEB) | 2030 Modeled Tons/Day | 2030 MVEB Request
NOx | 170.15 | 37.57 | 58 (+54%)
VOC | 81.76 | 32.67 | 52 (+59%)