## Slide 1: Drought Indicators Report
Georgia Environmental Protection Division
February 2016

## Slide 2: Background
Pursuant to the Rules for Drought Management, Section 391-3-3-.04 Drought Indicators and Triggers, the Director of EPD monitors climatic indicators and water supply conditions to assess drought occurrence and severity, and its impact upon the ability of public water systems to provide adequate supplies of water. These indicators and conditions may include, but not be limited, to the following:
U.S. Drought Monitor;
Precipitation;
Streamflow;
Groundwater;
Reservoir levels;
Short term climate predictions;
Soil moisture; and
Water supply conditions.

## Slide 3: Background
The Rules require EPD to report on current climatic indicators at least semi-annually or monthly when any part of the state has experienced at least two consecutive months of severe drought.
This report compares current conditions to historical levels (and/or reservoir rule curves) for each of the following indicators:
  Precipitation during the prior 3, 6, and 12 months;
  Streamflow at the select United States Geological Survey gages;
  Groundwater levels at select United States Geological Survey monitoring wells; and
  Reservoir levels at Allatoona Lake, Lake Hartwell, Clarks Hill Lake, and Lake Lanier.
The following sections of this presentation provide the data and information sources analyzed by EPD in developing this drought indicators report for conditions as of December 31, 2015.

## Slide 4: Drought Indicator Analysis Summary
Drought Monitor - According to the US Drought Monitor, the only area of the state showing any signs of dryness are 14 counties along the coast which are experiencing abnormally dry conditions.
Precipitation - For most of the state, precipitation has been well above normal.
Streamflow - With the exception of some USGS gages in southeastern Georgia, where there has been less rainfall, streamflow measured at USGS gages in the rest of the state have been normal or above normal.
Groundwater – Groundwater levels throughout the state are mostly near, at, or above normal for this time of year.
Reservoir Levels – All of the state’s major reservoirs are at or near full pool or are operating around their operational rule curves.
Short-term Climate Prediction - The Climate Prediction Center outlook for February – April 2016 calls for an equal chance of above or below normal temperatures and above normal precipitation for most of the state.
Soil Moisture – While there is a slight deficit in soil moisture in southeastern Georgia due to abnormally dry conditions, abundant rainfall throughout the rest of state has resulted in soil moisture levels adequate for healthy plant growth.
Water Supplies – Water supplies were not assessed as part of this report since drought impacts would not be expected under the present conditions .

## Slide 5: US Drought Monitor
Data Source:
http://droughtmonitor.unl.edu/

## Slide 8: 3, 6, and 12 Month Percent of Normal Precipitation
Data Source:
http://climate.ncsu.edu/drought

## Slide 9: 3 Month Percent of Normal Precipitation

## Slide 10: 6 Month Percent of Normal Precipitation

## Slide 11: 12 Month Percent of Normal Precipitation

## Slide 12: Soil Moisture Conditions
Data Source:
http://nsstc.uah.edu/aosc/lawn_garden_se.html

## Slide 13
The lawn-and-garden moisture index measures the capacity of current soil moisture to sustain healthy lawns and gardens. Positive values on the scale indicate adequate precipitation while negative values indicate a precipitation deficit.

## Slide 14: Streamflow Conditions
Data Source:
USGS Website

## Slide 15: Current (Daily) Conditions of All Available USGS Gages

## Slide 16: Streamflow Monitoring
As shown on the following slide, EPD Monitors 34 USGS stream gages in 13 of the State’s major river basins to assess drought conditions.
These gages were selected because each has:
  Long-term and relatively complete records for recent decades; and
  Relatively low consumptive water use implications and streamflows are not heavily influenced by dams.
Note: Hydrologic conditions of major rivers with streamflows that are heavily influenced by dams can be assessed by reviewing status of major storage reservoirs

## Slide 17
8
6
5
4
3
1
2
7
Gage# Basin Gage Name
1 Tennessee LOOKOUT CREEK NEAR NEW ENGLAND
2 Tennessee NOTTELY RIVER NEAR BLAIRSVILLE
3 Coosa Chattooga River at Summerville
4 Coosa TALKING ROCK CREEK NEAR HINTON
5 Coosa Etowah River at Canton
6 Chattahoochee Chattahoochee River at Cornelia
7 Chattahoochee Chestatee River near Dahlonega
8 Chattahoochee New River at GA 100 NEAR CORINTH
9 Chattahoochee Upatoi Creek at Columbus
10 Flint Flint River at GA26 near Montezuma
11 Flint Flint River at Albany
12 Flint Ichawaynochaway Creek at Milford
13 Flint Spring Creek near Iron City
14 Ocmulgee ALCOVY RIVER ABOVE COVINGTON
15 Ocmulgee Ocmulgee River at Macon
16 Ocmulgee TOBESOFKEE CREEK NEAR MACON
17 Ocmulgee TUCSAWHATCHEE CREEK NEAR HAWKINSVILLE
18 Oconee MIDDLE OCONEE RIVER NEAR ATHENS
19 Oconee LITTLE RIVER NEAR EATONTON
20 Oconee Oconee River at Dublin
21 Altamaha OHOOPEE RIVER NEAR REIDSVILLE
22 Savannah CHATTOOGA RIVER NEAR CLAYTON
23 Savannah Broad River near Bell
24 Savannah BEAVERDAM CREEK NEAR SARDIS
25 Savannah BRIER CREEK AT MILLHAVEN
26 Ogeechee CANOOCHEE RIVER NEAR CLAXTON
27 Ogeechee Ogeechee River near Eden
28 Ochlockonee OCHLOCKONEE RIVER NEAR THOMASVILLE
29 Suwanee Withlacoochee River near Pinetta FL
30 Suwanee Alapaha River at Statenville
31 Suwanee SUWANNEE RIVER AT US 441, AT FARGO
32 Satilla Satilla River near Waycross
33 Satilla LITTLE SATILLA RIVER NEAR OFFERMAN
34 St Mary ST MARYS RIVER NEAR MACCLENNY FL
34
13
12
10
11
17
16
15
14
20
19
18
21
27
26
25
24
23
22
32
31
30
29
28
33
USGS Stream Gages Monitored by EPD to Assess Drought Conditions
9

## Slide 18: Streamflow Graphs
For each of the 34 gages, EPD has prepared a graph that shows monthly average streamflow from January 1, 2015 through December 31, 2015;
To help put these streamflow conditions into perspective, for comparison purposes, each graph also shows:
  Monthly average streamflows for the years 2007 and 2011 when streamflows were at or near recorded low levels across much of the state; and
  A statistical composite of historical conditions showing the “driest” 50, 20, 10, and 5 percent of all recorded monthly average stream flows at the same gage.

## Slide 19: How to Read the Streamflow Graphs Example #1: Etowah River at Canton
The streamflow graph for Gage #5, USGS Etowah River gage at Canton shows :
  Average stream flow for May 2015 was 1008 cfs. The statistical composite of all historical data for this gage shows that average streamflow in May has historically been lower than May 2015 about 50% of the time; about 50% of the time in May it has been higher.
  Average stream flow in May 2011 was 726 cfs. The statistical composite of all historical data for this gage shows that average streamflow for May has historically been lower than May 2011 only 20% of the time; 80% of the time in May it has been higher.
  Average stream flow in May 2007 was 512 cfs. The statistical composite of all historical data for this gage shows that average streamflow for May has historically been lower than May 2007 only 5% of the time; 95% of the time in May it has been higher.
  The lowest recorded average stream flow for May was 480 cfs.

## Slide 20: How to Read the Streamflow Graphs Example #2: Flint River at Albany
The streamflow graph for Gage #11, USGS Flint River gage at Albany shows:
  Average stream flow for May 2015 was 3361 cfs. The statistical composite of all historical data for this gage shows that average streamflow in May has historically been lower than May 2015 about 50% of the time; about 50% of the time in May it has been higher.
  Average stream flow in May 2011 was 1575 cfs. The statistical composite of all historical data for this gage shows that average streamflow for May has historically been lower than May 2011 only 10% of the time; 90% of the time in May it has been higher.
  Average stream flow in May 2007 was 1291 cfs. The statistical composite of all historical data for this gage shows that average streamflow for May equal to the historically lowest recorded average stream flow for May.

## Slide 21
Chart: Gage #1, USGS #03568933, Tennessee Basin, LOOKOUT CREEK NEAR NEW ENGLAND, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 372.8065 | 480.5517 | 421.9677 | 293.1333 | 104.3871 | 66.9667 | 40.9355 | 35.5484 | 36.8833 | 33.1774 | 95.3 | 227.5484
Driest 20% | 241.1484 | 247.9929 | 297.8452 | 198.1467 | 73.7613 | 43.0733 | 28.8968 | 21.9742 | 21.86 | 18.9935 | 35.94 | 81.1677
Driest 10% | 169.1613 | 167.8 | 153.4645 | 128.24 | 59.0839 | 34.82 | 24.8452 | 16.6871 | 18.7633 | 16.9419 | 25.01 | 62.5548
Driest 5% | 99.4323 | 122.1429 | 125.2323 | 85.8333 | 52.3548 | 27.6333 | 19.1419 | 13.694 | 15.3583 | 14.9073 | 20.0277 | 51.471
Minimum | 44.4839 | 106.8966 | 79.1935 | 77.3333 | 37.1935 | 17.5667 | 14.3871 | 11.5613 | 10.4567 | 8.7968 | 15.9667 | 36.0645
Yr2007 | 241.0968 | 112.0714 | 110.3871 | 128 | 49.2581 | 17.5667 | 24.871 | 11.5613 | 10.4567 | 8.7968 | 19.46 | 40.4839
Yr2011 | 241.2258 | 128.8571 | 1007.3871 | 775.5333 | 121.0323 | 54.1 | 33.1613 | 24.7778 | 483.1667 | 33.1935 | 347.2333 | 632.6774
Yr2015 | 363.1613 | 219.3793 | 367.4194 | 466.3 | 80.0645 | 42 | 67.7742 | 38.6774 | 26.9333 | 88.1379 | 266.6 | 1224.1667
Back to Map

## Slide 22
Chart: Gage #2, USGS #03550500, Tennessee Basin, NOTTELY RIVER NEAR BLAIRSVILLE, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 211.9677 | 255.2414 | 290.9032 | 259.5 | 197.4516 | 135.8 | 101.7419 | 90.6452 | 74.1667 | 81.1935 | 102.7 | 165.5161
Driest 20% | 123.8 | 171.7399 | 217.8516 | 194.1867 | 156.8903 | 105.4418 | 72.2258 | 63.0452 | 53.7267 | 52.5032 | 65.68 | 104.2
Driest 10% | 104.4516 | 156.3357 | 177.5742 | 165.48 | 146.5355 | 91.2667 | 61.5484 | 56.9806 | 49.92 | 47.271 | 53.42 | 74.8774
Driest 5% | 98.3806 | 141.1786 | 171.9613 | 134.8067 | 142.7613 | 82.3 | 58.1484 | 50.2774 | 41.5 | 42.2323 | 51.08 | 65.7742
Minimum | 52.7097 | 99.2857 | 120.6452 | 126.0333 | 89.5484 | 52.1 | 52.0968 | 44.3871 | 36.8667 | 31.4839 | 37.0667 | 56.8387
Yr2007 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Yr2011 | 146.5806 | 173.0714 | 429.9355 | 414.7667 | 203.6452 | 105.7333 | 72.2581 | 49.3226 | 53.1667 | 48.0968 | 146.7333 | 202.2258
Yr2015 | 196.8065 | 148.2759 | 152.5161 | 291.5 | 112.4839 | 80.8929 | 112.5161 | 81.0645 | 70.2667 | 265.3548 | 332.8667 | 663.1667
Back to Map

## Slide 23
Chart: Gage #3, USGS #02398000, Coosa Basin, Chattooga River at Summerville, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 469.129 | 597.8929 | 617.7097 | 471.6 | 238.7903 | 159.7833 | 133.4516 | 114.9032 | 102.4 | 98.5806 | 136.5333 | 281.871
Driest 20% | 290.8516 | 337.5143 | 391.9935 | 287.4 | 163.3355 | 121.8533 | 105.1484 | 96.5355 | 85 | 78.1484 | 88.44 | 156.7161
Driest 10% | 234.2581 | 260.75 | 331.7581 | 229.08 | 130 | 103.9967 | 87.1839 | 76.1065 | 76.9267 | 70.3032 | 74.4533 | 116.5323
Driest 5% | 152.0774 | 193.9724 | 229.1129 | 194.3333 | 119.7 | 97.2817 | 74.3177 | 69.1387 | 72.4233 | 67.6581 | 72.7317 | 88.2
Minimum | 106.4516 | 156.9286 | 166.2903 | 129.0333 | 90.6452 | 67.2667 | 64.9677 | 56.4194 | 61.3333 | 54.1935 | 61.2333 | 72.4516
Yr2007 | 329.9032 | 178.9286 | 214.0323 | 155.5333 | 92.3226 | 67.2667 | 70.0323 | 56.4194 | 75 | 63.1613 | 99.3 | 154.5484
Yr2011 | 338.1613 | 292 | 1211.6774 | 718.2333 | 211.2258 | 121.6667 | 138.0968 | 83.2581 | 282.1667 | 99.4194 | 396.3333 | 671.7097
Yr2015 | 422 | 272.4483 | 395.6774 | 435.1333 | 161 | 99.3667 | 115 | 101.4516 | 77.4333 | 113.6452 | 312.8 | 1621.2333
Back to Map

## Slide 24
Chart: Gage #4, USGS #02382200, Coosa Basin, TALKING ROCK CREEK NEAR HINTON, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 199.3226 | 242.8929 | 287.129 | 247.2333 | 178.2581 | 128.7667 | 92.0323 | 77.3548 | 64.8667 | 62.4516 | 83.8667 | 135.2903
Driest 20% | 140.9419 | 123.9492 | 159.9613 | 151.16 | 101.4323 | 75.2733 | 46.9419 | 33.6671 | 38.0147 | 39.4129 | 58.7533 | 95.0258
Driest 10% | 119.1871 | 99.6054 | 134.4065 | 127.32 | 87.5871 | 59.8 | 35.5419 | 23.4052 | 28.2773 | 36.8 | 41.9733 | 59.8774
Driest 5% | 83.4065 | 85.7071 | 105.2516 | 81.2567 | 58.7645 | 25.4773 | 25.3519 | 20.6106 | 22.1233 | 19.57 | 31 | 54.6871
Minimum | 33.9677 | 79.0345 | 82.5161 | 58.5 | 41.8387 | 23.1667 | 16.4194 | 8.6677 | 4.6733 | 7.6419 | 16.5133 | 27.7097
Yr2007 | 125.1935 | 96.7857 | 82.5161 | 58.5 | 41.8387 | 23.1667 | 17.8065 | 8.6677 | 4.6733 | 7.6419 | 16.5133 | 27.7097
Yr2011 | 84.8387 | 84.0357 | 305.3548 | 315.7333 | 121.5161 | 74.8333 | 47.871 | 26.8387 | 56.4667 | 38.2258 | 68.6552 | 108.2143
Yr2015 | 116.2222 | 133.5517 | 142.3548 | 234.3667 | 130.1613 | 76.2 | 62.4516 | 64.4194 | 46.9333 | 101.7097 | 235.8333 | 564.3
Back to Map

## Slide 25
Chart: Gage #5, USGS #02392000, Coosa Basin, Etowah River at Canton, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 1330.871 | 1745.8528 | 1777.0968 | 1728.6667 | 1262.2581 | 965.4667 | 790.5645 | 637.0806 | 552.0333 | 599.9839 | 662.7167 | 939.8452
Driest 20% | 905.7613 | 1045.6599 | 1283.2516 | 1150.3333 | 936.4194 | 700.9333 | 564.6581 | 421.3161 | 383.4 | 383.8387 | 485.4933 | 650.7484
Driest 10% | 730.1516 | 852.1714 | 1030.4613 | 872.2267 | 728.3323 | 469.1033 | 366.3419 | 313.1935 | 290.3333 | 298.7387 | 421.7467 | 553.8742
Driest 5% | 617.9113 | 766.9431 | 947.4468 | 754.6783 | 514.7952 | 428.77 | 311.3306 | 247.129 | 238.6533 | 236.3435 | 343.0133 | 457.1339
Minimum | 406.8065 | 609.6071 | 620.4194 | 536 | 449.8387 | 263.6333 | 210.8065 | 160.9355 | 129.5667 | 149.7097 | 196.6 | 342.1613
Yr2007 | 1596.0968 | 884.9643 | 1073.3871 | 745.7333 | 511.5484 | 358.6667 | 369.5484 | 184.7097 | 129.5667 | 149.7097 | 196.6 | 342.1613
Yr2011 | 611.0645 | 932.3214 | 1868.9032 | 1604 | 726 | 459.4333 | 336.5484 | 201.8065 | 340.6333 | 235.6129 | 461 | 790.1613
Yr2015 | 1597.5161 | 1095.8276 | 1024.8387 | 1677.2333 | 1008.2258 | 743.3333 | 706.3548 | 493.2258 | 368.2667 | 929.1613 | 2078.2667 | 2869.3333
Back to Interpretation
Back to Map

## Slide 26
Chart: Gage #6, USGS #02331600, Chatthoochee Basin, Chattahoochee River at Cornelia, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 872.2581 | 1027 | 1153.9677 | 1089.1333 | 809.2258 | 691.7667 | 512.4194 | 461.7581 | 432.4667 | 486.1452 | 533.4 | 678.0645
Driest 20% | 626.0129 | 632.6857 | 738.2968 | 698.32 | 553.0774 | 496.54 | 385.5484 | 285.9355 | 293.9267 | 338.8194 | 391.9467 | 446.5677
Driest 10% | 528.4065 | 571.4276 | 611.3806 | 548.0467 | 442.7613 | 339.72 | 282.529 | 228.8129 | 269.2533 | 230.071 | 312.32 | 359.9226
Driest 5% | 496.5484 | 464.95 | 527.4323 | 535.5667 | 369.7032 | 250.56 | 247.9484 | 182.7855 | 197.5183 | 193.1403 | 240.2133 | 340.3016
Minimum | 292.8387 | 425.6071 | 400.8065 | 184.7 | 121.7419 | 119.8333 | 87.1613 | 92.0645 | 98.6333 | 136.1613 | 71.4333 | 280.4516
Yr2007 | 1034.8065 | 584.2857 | 911.6774 | 546.0667 | 400.5484 | 303.2667 | 259.7097 | 139.0323 | 123.6333 | 162.0323 | 221.9667 | 347.4194
Yr2011 | 533.5161 | 717.4286 | 1474.3548 | 1119.9667 | 701.3548 | 495.6333 | 383.871 | 204.0323 | 262.3 | 213 | 444.1 | 671.7097
Yr2015 | 868.2903 | 662.6552 | 650.4839 | 1018.8333 | 663.7742 | 527.2667 | 474.5161 | 398.2903 | 320.9 | 725.129 | 1345.9333 | 1796.1667
Back to Map

## Slide 27
Chart: Gage #7, USGS #02333500, Chatahoochee Basin, Chestatee River near Dahlonega, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 414.9194 | 466.4107 | 518.4355 | 497.5667 | 369.1613 | 273.3667 | 205.1935 | 204.3871 | 172.1333 | 187.0323 | 213.5667 | 314.8065
Driest 20% | 290.4129 | 338.2571 | 373.7548 | 337.34 | 260.6 | 210.5133 | 157.1742 | 128.4 | 115.9867 | 115.7871 | 156.2733 | 213.9742
Driest 10% | 224.029 | 259.9957 | 297.3935 | 271.6067 | 208.7935 | 152.0467 | 138.071 | 96.9355 | 93.0467 | 94.6258 | 117.16 | 175.9419
Driest 5% | 195.9629 | 240.5179 | 258.8774 | 240.2933 | 173.7645 | 115.8367 | 113.6742 | 80.7774 | 86.3133 | 72.1097 | 106.6733 | 146.7742
Minimum | 119.1613 | 177.2857 | 196.7419 | 158.3667 | 132 | 94.0333 | 63.4194 | 63.4839 | 49.4667 | 63.5161 | 85.4 | 127.0968
Yr2007 | 583.1613 | 281.3214 | 421.129 | 247.1667 | 175.6129 | 127.4667 | 114.129 | 76.2903 | 58.7667 | 63.5161 | 85.4 | 133.7097
Yr2011 | 256 | 341.5714 | 694.4194 | 575.4333 | 337.6452 | 236.4667 | 198.4516 | 109.9032 | 111.5333 | 97.5484 | 211.6667 | 348.2258
Yr2015 | 395.871 | 285.7931 | 274.3871 | 517.1333 | 254.7742 | 214.3 | 217.0323 | 204.2258 | 137.8 | 416.871 | 695.8333 | 1043.2333
Back to Map

## Slide 28
Chart: Gage #8, USGS #02338660, Chattahoochee Basin, NEW RIVER AT GA 100, NEAR CORINTH
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 167.7097 | 231 | 266.5645 | 171.4833 | 89.0484 | 58.2167 | 46.4194 | 29.3906 | 28.6167 | 34.0161 | 78.7833 | 109.3387
Driest 20% | 98.0065 | 129.7414 | 158.3742 | 100.8067 | 54.9677 | 23.38 | 15.009 | 10.9342 | 9.3533 | 13.9806 | 42.2267 | 63.8903
Driest 10% | 83.7581 | 116.2 | 115.3613 | 71.79 | 45.6323 | 12.365 | 5.3548 | 6.0332 | 6.7896 | 5.0371 | 18.8957 | 58.1161
Driest 5% | 74.4274 | 99.4071 | 99.1145 | 62.995 | 41.3903 | 10.8628 | 3.9334 | 3.7412 | 4.8581 | 3.8882 | 11.6282 | 46.371
Minimum | 64.3226 | 87.4138 | 84.5161 | 40.4333 | 13.7968 | 4.5333 | 2.67 | 2.7645 | 2.7826 | 1.6111 | 2.4523 | 28.7226
Yr2007 | 185.7419 | 105.3571 | 84.5161 | 48.9333 | 13.7968 | 4.5333 | 17.5226 | 5.4323 | 9.0733 | 2.9377 | 2.4523 | 28.7226
Yr2011 | 87.7097 | 178.3571 | 253.5806 | 165.5 | 55.0968 | 13.1533 | 38.929 | 7.4355 | 9.38 | 4.4 | 18.3367 | 59.2258
Yr2015 | 172.6774 | 203.6207 | 140.3226 | 259.3333 | 122.5161 | 66.931 | 50.6452 | 24.5742 | 24.5667 | 22.6774 | 366.8929 | 753
Back to Map

## Slide 29
Chart: Gage #12, USGS #02353500, Flint Basin, Ichawaynochaway Creek at Milford, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 845.8065 | 1142.9655 | 1101.9355 | 872.4667 | 550.7097 | 477.6333 | 432.2903 | 371.2903 | 365.5 | 343.4839 | 425.3333 | 602.3226
Driest 20% | 567.2645 | 754.35 | 769.1613 | 560.9933 | 338.7419 | 263.1733 | 303.0839 | 219.4452 | 242.8933 | 230.1355 | 296.2267 | 410.0968
Driest 10% | 457.2065 | 472.0106 | 612.0323 | 460.86 | 244.1355 | 164.7667 | 193.6258 | 142.8258 | 160.5733 | 179.5419 | 271.2533 | 369.7484
Driest 5% | 350.0065 | 445.5429 | 524.1484 | 377.9867 | 161.3871 | 93.2267 | 101.6839 | 118.0177 | 146.12 | 140.7742 | 214.0867 | 328.1
Minimum | 247 | 371 | 315.4839 | 248.7333 | 71.4839 | 24.7733 | 14.3774 | 58.4839 | 80.5 | 115.0645 | 111.7 | 241
Yr2007 | 805.5161 | 830.1786 | 475.9355 | 602.5 | 95.9677 | 77.3333 | 96.6129 | 58.4839 | 103 | 123.8065 | 156.6333 | 379.9677
Yr2011 | 515.3226 | 814.1786 | 589.4839 | 401.6 | 71.4839 | 24.7733 | 210.7097 | 93.8065 | 80.5 | 115.0645 | 168.1333 | 292.4194
Yr2015 | 925.5161 | 814.4483 | 803.3548 | 972.7 | 415.7097 | 348.6 | 240.6774 | 200.8065 | 273.0333 | 305.0645 | 863.5667 | 1554.4333
Back to Map

## Slide 30
Chart: Gage #10, USGS #02349605, Flint Basin, Flint River at GA26 near Montezuma, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 4122.9032 | 5364.6429 | 5921.2903 | 4496.3333 | 2677.4194 | 2119 | 2004.8387 | 1797.0968 | 1440 | 1282.9032 | 1695 | 2720.8065
Driest 20% | 2539.0323 | 3324.1379 | 3609.0323 | 2952.6667 | 1748.9355 | 1278.1333 | 1291.0258 | 1159.5419 | 967.04 | 925.4968 | 1241.0667 | 1818.8387
Driest 10% | 2225.8065 | 2518.6207 | 3088.3871 | 2346 | 1547.0968 | 986.8733 | 879.1419 | 804.8742 | 823.7533 | 758.6323 | 1039.7133 | 1522.3871
Driest 5% | 1891.129 | 2393.1096 | 2780 | 2123.6667 | 1256.9677 | 764.6733 | 679.5177 | 644.3774 | 717.495 | 706.4968 | 919.2333 | 1447.3048
Minimum | 1442.9032 | 1758.5714 | 2002.5806 | 1212.2333 | 840.3226 | 509.4667 | 476.7419 | 506.4839 | 491.2667 | 574.871 | 503.7 | 1100.129
Yr2007 | 3575.4839 | 2782.5 | 3798.3871 | 1750.6667 | 860.2258 | 584.3 | 753.2903 | 538.6452 | 735.7667 | 574.871 | 608.3667 | 1225.3226
Yr2011 | 1921.9355 | 4405.7143 | 4048.7097 | 3415.6667 | 1388.8387 | 791.4333 | 873.9355 | 670.7419 | 665.7 | 720.129 | 816.3333 | 1397.9677
Yr2015 | 3456.4516 | 3625.5172 | 3849.0323 | 6291 | 2428.0645 | 2230.6667 | 1295.871 | 1156.3793 | 1481.6667 | 1333.0968 | 5579 | 12016.3333
Back to Map

## Slide 31
Chart: Gage #11, USGS #02352500, Flint Basin, FLINT RIVER AT ALBANY, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 7118.7097 | 9749.2857 | 10672.2581 | 7619 | 4388.0645 | 3615.3333 | 3498.3871 | 3235.4839 | 2481 | 2385.9032 | 2876.0667 | 4422.5806
Driest 20% | 4367.1613 | 5855.5 | 6352.8387 | 4772.0667 | 2820.1935 | 2180.2 | 2239.0968 | 2012.2 | 1724.6867 | 1628.2581 | 1950.4 | 2788.129
Driest 10% | 3628.129 | 4130.3448 | 5232.9677 | 4114.1333 | 2313.4194 | 1768.32 | 1337.8387 | 1336.8935 | 1488.4533 | 1443.5935 | 1779.5067 | 2465.0323
Driest 5% | 3211.3871 | 3701.0628 | 4511.6452 | 3477.3667 | 1994.0645 | 1199.0033 | 1064.9129 | 953.0694 | 1248.6067 | 1193.5806 | 1473.3367 | 2327.3226
Minimum | 2305.9677 | 2966.0714 | 3184.1935 | 2036 | 1218.1613 | 758.6 | 643.871 | 838 | 764.1333 | 976.0323 | 1055.0667 | 1418
Yr2007 | 6215.4839 | 5591.4286 | 5568.3871 | 3310.3333 | 1290.9355 | 1045.0333 | 1324.6129 | 987.4839 | 1384.9667 | 1104.4194 | 1118.7 | 2463.2258
Yr2011 | 3207.0968 | 6534.2857 | 5465.8065 | 4788.6667 | 1575.1935 | 758.6 | 1282.9032 | 951.2581 | 764.1333 | 976.0323 | 1171.3333 | 2099.6774
Yr2015 | 6474.1935 | 6682.7586 | 6799.3548 | 9186.3333 | 3361.2903 | 2884.3333 | 1885.4839 | 1849.0323 | 2216 | 2074.1935 | 7012.6667 | 15453.6667
Back to Map
Back to Interpretation

## Slide 32
Chart: Gage #12, USGS #02353500, Flint Basin, Ichawaynochaway Creek at Milford, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 845.8065 | 1142.9655 | 1101.9355 | 872.4667 | 550.7097 | 477.6333 | 432.2903 | 371.2903 | 365.5 | 343.4839 | 425.3333 | 602.3226
Driest 20% | 567.2645 | 754.35 | 769.1613 | 560.9933 | 338.7419 | 263.1733 | 303.0839 | 219.4452 | 242.8933 | 230.1355 | 296.2267 | 410.0968
Driest 10% | 457.2065 | 472.0106 | 612.0323 | 460.86 | 244.1355 | 164.7667 | 193.6258 | 142.8258 | 160.5733 | 179.5419 | 271.2533 | 369.7484
Driest 5% | 350.0065 | 445.5429 | 524.1484 | 377.9867 | 161.3871 | 93.2267 | 101.6839 | 118.0177 | 146.12 | 140.7742 | 214.0867 | 328.1
Minimum | 247 | 371 | 315.4839 | 248.7333 | 71.4839 | 24.7733 | 14.3774 | 58.4839 | 80.5 | 115.0645 | 111.7 | 241
Yr2007 | 805.5161 | 830.1786 | 475.9355 | 602.5 | 95.9677 | 77.3333 | 96.6129 | 58.4839 | 103 | 123.8065 | 156.6333 | 379.9677
Yr2011 | 515.3226 | 814.1786 | 589.4839 | 401.6 | 71.4839 | 24.7733 | 210.7097 | 93.8065 | 80.5 | 115.0645 | 168.1333 | 292.4194
Yr2015 | 925.5161 | 814.4483 | 803.3548 | 972.7 | 415.7097 | 348.6 | 240.6774 | 200.8065 | 273.0333 | 305.0645 | 863.5667 | 1554.4333
Back to Map

## Slide 33
Chart: Gage #13, USGS #02357000, Flint River, Spring Creek near Iron City, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 457.6935 | 839.9477 | 1053.7258 | 629.4 | 269.1935 | 180.2 | 158.2581 | 166.0161 | 139.3333 | 112.7097 | 107.3333 | 167.6129
Driest 20% | 146.9161 | 285.7251 | 452.2065 | 321.4933 | 160.6516 | 66.8 | 54.4765 | 48.471 | 48.4467 | 36.3226 | 46.4667 | 68.0258
Driest 10% | 93.7548 | 169.6679 | 318.1194 | 227.2433 | 72.0581 | 40.9267 | 32.5935 | 20.9771 | 22.4467 | 13.9355 | 23.65 | 50.4774
Driest 5% | 47.1532 | 121.6 | 253.1952 | 198.1583 | 43.0542 | 10.6253 | 5.1275 | 9.6559 | 18.35 | 10.529 | 11.1691 | 20.7351
Minimum | 21.729 | 64.6071 | 78.6452 | 148.4 | 20.5581 | 0.9563 | 0.24895 | 0.16667 | 0.1175 | 1.0613 | 0.1325 | 13.4839
Yr2007 | 791.2903 | 915.3214 | 630 | 316.4 | 40.1742 | 2.2983 | 0.24895 | 0 | 0 | 0 | 0 | 60.1071
Yr2011 | 35.9032 | 226.6786 | 248.6452 | 219.9333 | 20.5581 | 0.9563 | 54.5361 | 10.6463 | 0 | 0 | 0 | 15.1833
Yr2015 | 750.9677 | 581.4483 | 570.3548 | 598.9333 | 304.6129 | 139.8667 | 97.1935 | 34.6161 | 29.3567 | 39.0645 | 567.4333 | 971.4333
Back to Map

## Slide 34
Chart: Gage #14, USGS #02208450, Ocumulgee Basin, ALCOVY RIVER ABOVE COVINGTON, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 302.871 | 405.1034 | 387.8065 | 258.3 | 185.8387 | 135.0667 | 91.7097 | 94.871 | 95 | 95 | 137.5 | 200.4516
Driest 20% | 171.3226 | 206.3214 | 202.7097 | 172.3333 | 94.9677 | 63.6333 | 43.6452 | 30.7097 | 36.7 | 58.3226 | 80.3333 | 111.6774
Driest 10% | 137.9355 | 155.9286 | 191.871 | 147.7 | 55.129 | 25.6933 | 23.5774 | 23.5968 | 19.0862 | 28.3226 | 47.6667 | 87.2258
Driest 5% | 121.9677 | 128.7143 | 177.4194 | 100.0667 | 49.8065 | 23.5655 | 9.8158 | 20.9 | 15.2183 | 24.3323 | 38.2667 | 83.0645
Minimum | 74.8387 | 76.5 | 117.5484 | 42.6 | 36.6774 | 7.8867 | 5.9135 | 9.1355 | 10.7367 | 7.6613 | 27.7667 | 45.871
Yr2007 | 258.2258 | 166.5357 | 240.4516 | 98.4333 | 55.129 | 29.9 | 43.6452 | 30.7935 | 27.76 | 16.8065 | 27.7667 | 45.871
Yr2011 | 121.9677 | 322.25 | 449.2581 | 282.4667 | 94.9677 | 52.6667 | 52.7742 | 25.6194 | 15.2183 | 27.0032 | 53.2 | 81.25
Yr2015 | 197.7742 | 190.1379 | 169.4516 | 456.9 | 136.3871 | 131.8667 | 98.1935 | 209.9032 | 106.7 | 227.0323 | 777.9 | 933.9667
Back to Map

## Slide 35
Chart: Gage #15, USGS #02213000, Ocmulgee Basin, Ocmulgee River at Macon, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 3001.6129 | 4266.4286 | 4494.1935 | 3221.3333 | 2119.0323 | 1596.5333 | 1467.0484 | 1257.9032 | 1019.1 | 1055.0968 | 1266.9333 | 2160.7097
Driest 20% | 1757.2129 | 2432.9557 | 2597.5484 | 2184.3067 | 1357.0516 | 987.2867 | 898.2194 | 815.1742 | 668.1867 | 664.0516 | 805.9867 | 1271.9484
Driest 10% | 1438.7484 | 1690.8143 | 2189.0323 | 1736.8467 | 1102.4968 | 738.9667 | 638.8355 | 565.1806 | 531.8333 | 504.9419 | 607.42 | 1032.0516
Driest 5% | 1321.5065 | 1475.0533 | 1768.129 | 1477.8067 | 833.8645 | 536.64 | 497.0645 | 432.9806 | 392.9867 | 386.2226 | 419.3633 | 868.3645
Minimum | 749.8065 | 1084.6786 | 1318.8387 | 779.3667 | 519.6774 | 300.7333 | 214.4194 | 298.5806 | 295.7333 | 164.7742 | 186.2667 | 617.5484
Yr2007 | 2717.7419 | 1655.3571 | 3009.3871 | 1142.3 | 658.9032 | 445.8 | 630.5484 | 435.6452 | 489.5667 | 397.2258 | 341.2667 | 741.8387
Yr2011 | 1707.4194 | 3844.6429 | 4278.7097 | 3419.2333 | 1102.871 | 653.5 | 651.5161 | 366.9355 | 392 | 336.5806 | 559.9667 | 1137.871
Yr2015 | 2410.8065 | 2962.931 | 2642.2581 | 6047.3333 | 1829.8387 | 1537.3 | 880 | 1097.7097 | 1109 | 1320.9355 | 6713.6667 | 10101.4815
Back to Map

## Slide 36
Chart: Gage #16, USGS #02213500, Ocmulgee Basin, TOBESOFKEE CREEK NEAR MACON, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 233.6452 | 332.2069 | 355.6774 | 229.6667 | 118.8065 | 93.1 | 73.129 | 59.5806 | 45.1 | 38.5484 | 58.6 | 139.129
Driest 20% | 114.9677 | 145.7357 | 170.8065 | 137.8133 | 69.071 | 50.6733 | 33.7097 | 27.071 | 21.5393 | 18.8387 | 29.4267 | 72.9806
Driest 10% | 100.5097 | 118.1749 | 139.3652 | 110.2493 | 46.2877 | 34.38 | 20.3239 | 21.0645 | 16.4667 | 12.5277 | 18.3733 | 52.871
Driest 5% | 76.8935 | 96.8 | 105.0323 | 75.7343 | 36.251 | 13.0473 | 12.9303 | 13.2513 | 9.817 | 9.0452 | 16.904 | 31.6939
Minimum | 43.6452 | 28.5 | 43.3226 | 31.1 | 10.7839 | 4.9133 | 7.9323 | 5.9226 | 4.8033 | 5.9677 | 8.2767 | 9.1677
Yr2007 | 151.5806 | 131.1071 | 301.7419 | 65.0033 | 12.2097 | 4.9133 | 8.5968 | 5.9226 | 6.1767 | 20.1194 | 18.13 | 107.3516
Yr2011 | 102.1935 | 257.7857 | 250.871 | 159.5667 | 30.7097 | 12.1 | 14.7419 | 14.2161 | 11.47 | 9.5194 | 10.2967 | 46.2581
Yr2015 | 108.8387 | 228.3103 | 173.7419 | 333.5333 | 117.2258 | 75.92 | 34.8323 | 48.5258 | 51.1667 | 47.9355 | 213.5 | 1017.1667
Back to Map

## Slide 37
Chart: Gage #17, USGS #02215100, Ocmulgee Basin, TUCSAWHATCHEE CREEK NEAR HAWKINSVILLE, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 168.7097 | 257.8584 | 220.2097 | 144.7 | 54.3871 | 55.2667 | 27.9823 | 19.329 | 19.465 | 23.7548 | 32.6833 | 56.7097
Driest 20% | 72.9032 | 107.7241 | 130.871 | 77.2667 | 22.1613 | 11.74 | 13.1742 | 5.9968 | 9.6 | 10.6742 | 20.7333 | 36.9355
Driest 10% | 50.0323 | 56.5 | 107.0806 | 60.6167 | 15.6823 | 9.1317 | 6.0403 | 5.1115 | 7.6933 | 7.1935 | 13.995 | 31.0806
Driest 5% | 41.7097 | 52.7679 | 98.5 | 54.9833 | 12.0597 | 7.5017 | 4.5161 | 2.6013 | 3.3547 | 3.7161 | 9.8733 | 17.7976
Minimum | 27 | 47.4286 | 70.8065 | 30.99 | 7.1419 | 3.76 | 1.3245 | 0.89304 | 0.018 | 0.99258 | 4.0033 | 11.0258
Yr2007 | 176.129 | 161.75 | 108.3548 | 54.4667 | 13.5935 | 12.5333 | 14.2194 | 12.0032 | 13.9433 | 7.9129 | 9.5567 | 51.5484
Yr2011 | 47.8065 | 261.7857 | 135.7097 | 95.2667 | 11.5484 | 3.76 | 4.1871 | 0.89304 | 0.018 | 0.99258 | 4.0033 | 13.5581
Yr2015 | 326.5806 | 413.1034 | 282.2258 | 366.3667 | 139.5484 | 59.4667 | 29.8065 | 53.2903 | 24.4667 | 24.2258 | 103.2667 | 354.1667
Back to Map

## Slide 38
Chart: Gage #18, USGS #02217500, Oconee Basin, MIDDLE OCONEE RIVER NEAR ATHENS, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 559.0645 | 681.4107 | 811.0645 | 607.7667 | 437.8548 | 347.65 | 270.8871 | 232.8226 | 203.8833 | 216.9839 | 273.4833 | 423.4516
Driest 20% | 378.3677 | 459.8478 | 510.5419 | 407.5667 | 271.0839 | 208.9467 | 160 | 109.4968 | 132.3133 | 149.6323 | 201.0467 | 262.5161
Driest 10% | 309.2516 | 346.0217 | 394.8516 | 339.3167 | 195.0548 | 147.2733 | 99.4387 | 68.201 | 79.7533 | 82.0032 | 138.61 | 214.2806
Driest 5% | 258.0371 | 273.8339 | 360.8355 | 298.6217 | 167.6323 | 106.68 | 61.7419 | 52.5645 | 48.225 | 60.6774 | 101.4417 | 194.4984
Minimum | 140.4194 | 151.0714 | 285.3871 | 187.3214 | 143.9333 | 63.5667 | 25.3097 | 36.4194 | 41.1 | 29.5839 | 69 | 118.3548
Yr2007 | 553.6774 | 366.8571 | 531.871 | 236.6 | 147.871 | 79.9333 | 100.4839 | 50.6452 | 41.6 | 29.5839 | 69.6333 | 133.6774
Yr2011 | 330.4839 | 627.1071 | 906.7742 | 602.2 | 250.4194 | 151.6667 | 97 | 42.1613 | 48.5 | 59.5806 | 97.9 | 236.129
Yr2015 | 476.3548 | 459.6897 | 490.4194 | 744.2667 | 324.6129 | 267.4333 | 197 | 271.9355 | 183.3 | 432.9355 | 1391.2333 | 1132.5769
Back to Map

## Slide 39
Chart: Gage #19, USGS #02220900, Oconee Basin, LITTLE RIVER NEAR EATONTON, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 264.7419 | 380 | 337.2258 | 240.0667 | 131 | 109.7333 | 63 | 58.7742 | 49.5667 | 60.2581 | 85.5667 | 138.5161
Driest 20% | 119.2903 | 211.7537 | 229.529 | 156.3533 | 73.8258 | 30.7933 | 22.4742 | 18.3116 | 23.6267 | 23.5032 | 45.44 | 92.5596
Driest 10% | 104.7677 | 172.6214 | 181.3677 | 112.4733 | 59.7871 | 19.1793 | 16.9013 | 9.8677 | 14.9567 | 16.6826 | 37.7147 | 71.1742
Driest 5% | 95.4903 | 155.2321 | 169.0161 | 90.24 | 34.229 | 14.0633 | 14.9242 | 5.9511 | 7.138 | 10.9472 | 34.53 | 58.5355
Minimum | 77.6129 | 101.1429 | 142.3548 | 61.8 | 32.5806 | 10.8667 | 1.4135 | 3.9839 | 3.64 | 6.0065 | 21.2 | 54.6774
Yr2007 | 256.3226 | 168.6071 | 329.1613 | 80.3 | 33.2581 | 13.2233 | 18.4323 | 6.1223 | 7.49 | 6.0226 | 33.9 | 56.5484
Yr2011 | 182.9032 | 327.8214 | 337.2258 | 263.7667 | 73.7742 | 25.5667 | 31.1935 | 10.7097 | 6.3167 | 13.0577 | 34.8 | 92.3462
Yr2015 | 232.8387 | 287.4828 | 279.0968 | 402.5667 | 117.2258 | 64.9333 | 32.9355 | 43.8323 | 50.6333 | 88.3226 | 450.7333 | 1279.2333
Back to Map

## Slide 40
Chart: Gage #20, USGS #02223500, Oconee Basin, Oconee River at Dublin, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 5634.1935 | 7923.7931 | 7911.9355 | 5628.6667 | 3240.3226 | 2415.5 | 2386.7742 | 2041.9032 | 1627.5 | 1798.0645 | 2050.6667 | 3503.5484
Driest 20% | 3132.0645 | 4456.1429 | 4913.2258 | 3449.2667 | 1921.929 | 1571.4 | 1259.4839 | 1122.3871 | 968.7667 | 836.5419 | 1293.4867 | 2062.6774
Driest 10% | 2551.2903 | 3484.5517 | 3933.9355 | 2848.4 | 1517.3935 | 1016.4267 | 912.0387 | 700.529 | 783.8667 | 646.7806 | 1053.4133 | 1661.0839
Driest 5% | 1995.771 | 3025.383 | 3158.6774 | 2355.6667 | 1236.3935 | 632.8833 | 498.9548 | 508.1581 | 621.1067 | 528.9774 | 712.3333 | 1059.5065
Minimum | 1176.9355 | 1683.1429 | 2580 | 814.9333 | 463.0968 | 440.0667 | 361.1935 | 329.0323 | 307.2 | 348.871 | 378.7667 | 760.5484
Yr2007 | 4757.7419 | 3400 | 6195.8065 | 1815.8667 | 690.0968 | 648.7333 | 518.1935 | 416.3871 | 558.2667 | 439.9032 | 415.7333 | 981.3548
Yr2011 | 2544.8387 | 5939.2857 | 5638.3871 | 5164.6667 | 1319.4516 | 595.2333 | 396.2903 | 329.0323 | 307.2 | 348.871 | 412.1 | 815.7097
Yr2015 | 4038.7097 | 4795.5172 | 4892.2581 | 6338 | 1673.9677 | 1517.4333 | 895.6129 | 1407.6774 | 1311.0333 | 3193.871 | 8192 | 13587.6667
Back to Map

## Slide 41
Chart: Gage #21, USGS #02225500, Altamaha Basin, OHOOPEE RIVER NEAR REIDSVILLE, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 1060.9677 | 1835.2414 | 2032.871 | 1364.8333 | 556.4516 | 275.4 | 226.129 | 214.6129 | 252.2667 | 172.4194 | 136.8333 | 333
Driest 20% | 385.6129 | 788.8571 | 991.9355 | 492.2867 | 138 | 92.7867 | 88.1032 | 88.3161 | 65.1133 | 54.871 | 57.9133 | 167.0323
Driest 10% | 183.8903 | 522.8719 | 699.1613 | 327.7467 | 88.0065 | 57.8533 | 42.8194 | 49.129 | 46.4867 | 35.0194 | 47.3733 | 84.8839
Driest 5% | 129.0645 | 267.9265 | 471.4806 | 252.0533 | 69.1387 | 44.61 | 40.0419 | 42.5161 | 39.6433 | 31.5968 | 34.7 | 63.3194
Minimum | 46.9032 | 109.4815 | 173.5161 | 85.6 | 30.7407 | 27.2 | 27.0968 | 27.9677 | 23 | 20.8065 | 24.4667 | 29.7742
Yr2007 | 1033.4516 | 1756.3929 | 931.5806 | 532.3 | 88.4839 | 526.7 | 140.5806 | 89.3871 | 418.7667 | 120.0645 | 57.4333 | 333
Yr2011 | 259.2903 | 1632.9286 | 820.5484 | 1056.3 | 57.6129 | 39.5667 | 40.6774 | 27.9677 | 23.0333 | 26.6774 | 25.3667 | 35.1613
Yr2015 | 1512.3871 | 1773.4483 | 2575.1613 | 1999.9333 | 737.7419 | 218.6333 | 81.1935 | 65.7586 | 98.3667 | 107.1935 | 808.3333 | 1222.8
Back to Map

## Slide 42
Chart: Gage #22, USGS #02177000, Savannah Basin, CHATTOOGA RIVER NEAR CLAYTON, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 737.9677 | 805.6552 | 849.6774 | 827.1 | 620.6452 | 537.6333 | 420.5161 | 379.6129 | 348.3667 | 352.2903 | 399.3667 | 590.6774
Driest 20% | 475.4129 | 509.5985 | 608.2452 | 590.96 | 471.4968 | 377.0133 | 279.6065 | 242.7032 | 240.3467 | 219.1677 | 275.8667 | 370.3613
Driest 10% | 406.2065 | 484.55 | 512.3742 | 484.7333 | 415.929 | 278.5133 | 248.6452 | 194.5548 | 178.1533 | 183.0774 | 231.18 | 306.4581
Driest 5% | 322.2065 | 413.2357 | 456.2 | 421.58 | 321.1806 | 236.92 | 216.6452 | 173.271 | 169.6867 | 146.6065 | 185.8467 | 252.6774
Minimum | 155.3226 | 346.6786 | 387.4194 | 349.4333 | 261.1613 | 202.0333 | 143.2903 | 152.3871 | 117.9333 | 98.6452 | 155.2 | 182.9032
Yr2007 | 1009.4839 | 425.4643 | 638.1613 | 394.6 | 282.6129 | 214.6667 | 212.4839 | 152.3871 | 121.8333 | 148.4516 | 161.4667 | 280.1613
Yr2011 | 373.9355 | 510.3929 | 1268.6129 | 1058.7 | 626.1613 | 372.8 | 314.3871 | 177.5484 | 245.1333 | 138.0968 | 390.0333 | 775.0968
Yr2015 | 768.3226 | 561.2414 | 607.1935 | 917.2 | 479.5484 | 339 | 245.9032 | 231.3548 | 219.8333 | 526.0323 | 1068.3 | 1778.8667
Back to Map

## Slide 43
Chart: Gage #23, USGS #02192000, Savannah Basin Broad River near Bell, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 1914.8387 | 2353.4483 | 2703.5806 | 1940 | 1399.3548 | 1111.1667 | 901.1129 | 804.6129 | 731.4333 | 781.5806 | 940.25 | 1349.3548
Driest 20% | 1250.3677 | 1512.734 | 1780.8065 | 1364.04 | 913.4065 | 751.6333 | 643.9226 | 432.329 | 445.2467 | 472.271 | 567.4333 | 887.8581
Driest 10% | 1014.4065 | 1274.6429 | 1494.671 | 1171.86 | 684.8065 | 447.9467 | 378.8742 | 276.7613 | 314.8333 | 297.9548 | 468.75 | 763.3097
Driest 5% | 893.2677 | 914.7683 | 1273.5484 | 1062.0833 | 537.7774 | 332.0567 | 228.1452 | 214.7065 | 240.2833 | 230.8661 | 383.625 | 638.3613
Minimum | 505.9677 | 762.75 | 969.5161 | 519.2667 | 369.0645 | 238.4 | 162 | 89.1613 | 157.1333 | 148.1613 | 207.5333 | 455.2581
Yr2007 | 2217.7419 | 1330.3571 | 2703.5806 | 887.6 | 676.0645 | 339.1667 | 361.871 | 188.9032 | 157.1333 | 158.5484 | 217 | 503.0968
Yr2011 | 1025.5806 | 2090 | 2862.5806 | 1673.3333 | 719.7742 | 440.6 | 267.5161 | 195.0323 | 160.7333 | 205.6452 | 382.2 | 762.129
Yr2015 | 1570.9677 | 1642.5862 | 1532.2581 | 2345.6667 | 779.52 | 741.7333 | 569.6774 | 512.5806 | 444.6333 | 1933.129 | 5298.6667 | 6922.6667
Back to Map

## Slide 44
Chart: Gage #24, USGS #02198100, Savannah Basin, BEAVERDAM CREEK NEAR SARDIS, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 16.25 | 34.6539 | 40.5694 | 16.7983 | 6.1581 | 5.7733 | 5.0371 | 3.9113 | 4.4417 | 4.9452 | 6.6183 | 10.3887
Driest 20% | 8.2484 | 10.2448 | 15.4097 | 7.8767 | 4.4516 | 4.36 | 3.3645 | 3.229 | 3.3733 | 3.5871 | 4.84 | 5.529
Driest 10% | 6.7597 | 9.5875 | 10.9661 | 5.9183 | 4.1516 | 3.7683 | 3.0387 | 2.9548 | 3.1817 | 3.4758 | 4.0433 | 4.9758
Driest 5% | 5.3444 | 8.3679 | 8.9403 | 4.7433 | 3.3935 | 3.2767 | 2.9556 | 2.7589 | 3.0825 | 2.7847 | 3.6367 | 4.9532
Minimum | 3.9387 | 4.325 | 5.2968 | 4.3033 | 3.1387 | 2.5833 | 2.1323 | 2.6419 | 2.6367 | 2.2355 | 2.7733 | 4.1419
Yr2007 | 20.9032 | 32.7143 | 17.6258 | 13.94 | 5.7097 | 7.9367 | 3.7935 | 3.5645 | 3.3733 | 3.8419 | 3.54 | 12.0129
Yr2011 | 5.1161 | 13.7643 | 12.6871 | 13.1033 | 3.2 | 2.5833 | 3.0419 | 2.6419 | 2.6367 | 2.5581 | 3.9267 | 4.1419
Yr2015 | 61.9032 | 96.9655 | 86.871 | 66.6 | 8.5194 | 7.7967 | 7.4613 | 5 | 5.04 | 29.3645 | 66.0667 | 44.2857
Back to Map

## Slide 45
Chart: Gage #25, USGS #02198000 , Savannah Basin, BRIER CREEK AT MILLHAVEN, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 719.0645 | 866.7931 | 1017.8065 | 774.7333 | 434.1935 | 342.0667 | 299.6774 | 287.7419 | 274.6667 | 299.8387 | 325.3333 | 491.9355
Driest 20% | 470.4258 | 551.25 | 615.4581 | 464.9 | 237.8387 | 219.0467 | 178.0516 | 165.671 | 167.1133 | 193.2645 | 254.7 | 373.6258
Driest 10% | 433.7161 | 496.2547 | 488.0903 | 345.4333 | 183.471 | 156.1733 | 120.3613 | 138.9871 | 148.06 | 153.3097 | 225.0933 | 312.1677
Driest 5% | 340.9613 | 369.6036 | 440.6452 | 296.69 | 150.2194 | 131.9533 | 97.8548 | 111.8774 | 132.8 | 112.4032 | 177.87 | 233.8452
Minimum | 204.1613 | 210.5714 | 315.6129 | 127.9667 | 100 | 69.5333 | 61.129 | 49.5484 | 48.5667 | 93.5484 | 107.6333 | 175.129
Yr2007 | 719.0645 | 638.0357 | 765.2903 | 345.8333 | 149.9032 | 203.6 | 109.6129 | 103.6129 | 133.3 | 95.4194 | 108.1 | 299.4194
Yr2011 | 321.6452 | 628.0357 | 445 | 464.3667 | 150.3548 | 69.5333 | 93.6774 | 49.5484 | 48.5667 | 99.8387 | 124.3 | 175.129
Yr2015 | 664.1935 | 648.4828 | 944.0645 | 774.6667 | 259.7742 | 176.8333 | 139.8387 | 112.4839 | 177.9333 | 573.9677 | 932.4667 | 925.6333
Back to Map

## Slide 46
Chart: Gage #26, USGS #02203000, Ogeechee Basin, CANOOCHEE RIVER NEAR CLAXTON, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 462.3548 | 786.069 | 806.4194 | 547.6 | 183.5484 | 111.5 | 94.9677 | 108.9032 | 81.1667 | 76.6129 | 57.8333 | 136.1613
Driest 20% | 184.5032 | 283.9429 | 414.4516 | 182.3733 | 38.7794 | 12.758 | 11.1058 | 11.3626 | 9.6673 | 7.4232 | 9.046 | 52.1484
Driest 10% | 50.8 | 157.5143 | 254.2645 | 91.8 | 14.5516 | 5.798 | 4.8297 | 5.4465 | 5.0673 | 2.9852 | 4.4669 | 17.031
Driest 5% | 35.4439 | 101.8196 | 152.8548 | 60.8147 | 7.6781 | 4.5593 | 2.7597 | 2.7491 | 2.0707 | 2.3201 | 3.0612 | 7.7784
Minimum | 2.0516 | 8.3643 | 52.6129 | 42.12 | 2.2613 | 1.6103 | 1.5616 | 1.3455 | 1.2013 | 1.22 | 1.514 | 1.1871
Yr2007 | 402.871 | 734.3929 | 360.5161 | 225.2 | 13.1161 | 187.1533 | 13.4323 | 11.4935 | 77.8667 | 17.4774 | 6.9467 | 100.2452
Yr2011 | 33.1677 | 452.1071 | 249.3226 | 380.2333 | 7.4161 | 2.243 | 2.0861 | 3.2171 | 1.495 | 1.2913 | 2.2477 | 3.5516
Yr2015 | 865.6129 | 1011.7241 | 1360.5484 | 976.2667 | 273.3548 | 32.9333 | 20.4935 | 5.7161 | 3.51 | 14.1645 | 226.2133 | 403.8333
Back to Map

## Slide 47
Chart: Gage #27, USGS #02202500, Ogeechee Basin, Ogeechee River near Eden, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 2344.1935 | 3286.8966 | 4146.7742 | 3040.3333 | 1563.3548 | 1037.0167 | 825.7258 | 812.6452 | 692.3333 | 571.0645 | 590.9667 | 1124.5747
Driest 20% | 1063.8839 | 1830.7143 | 2305.871 | 1703.5267 | 725.9806 | 573.1733 | 356.729 | 284.3226 | 312.34 | 323.0839 | 410.34 | 659.2387
Driest 10% | 905.4129 | 1421.0542 | 1661.0323 | 1203.4833 | 526.7548 | 305.6833 | 228.7871 | 219.3581 | 238.8667 | 214.7903 | 307.6633 | 525.5774
Driest 5% | 665.2 | 1033.9714 | 1315.8065 | 995.6 | 388.1952 | 270.7767 | 160.5242 | 206.271 | 194.66 | 165.2935 | 229.155 | 429.5645
Minimum | 374.5484 | 411.5714 | 863.9355 | 349.7 | 171.9355 | 118.8667 | 91.6129 | 87.7742 | 35.6333 | 128.1613 | 102.1667 | 258.871
Yr2007 | 1741.0645 | 2355.7143 | 2303.2258 | 1025.9333 | 395.129 | 715.3 | 267.8387 | 217.0323 | 310.2333 | 173.6774 | 139.9 | 469.2903
Yr2011 | 635.4194 | 2109 | 1332.2581 | 1895.0333 | 348.9032 | 118.8667 | 91.6129 | 87.7742 | 35.6333 | 146.1613 | 167.5667 | 300.0645
Yr2015 | 3176.129 | 2810.6897 | 4903.871 | 3141.6667 | 1583.6129 | 528.0667 | 266.9032 | 209.4839 | 300.4138 | 725.1935 | 2355.9 | 2204.2857
Back to Map

## Slide 48
Chart: Gage #28, USGS #02327500, Ochlockonee Basin, OCHLOCKONEE RIVER near THOMASVILLE, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 445.5806 | 652.1429 | 839.1935 | 526.6333 | 192 | 166.3667 | 244.1774 | 147.1613 | 117.0833 | 79.2097 | 32.625 | 129.0645
Driest 20% | 107.2194 | 263.35 | 357.2452 | 233.4867 | 52.7871 | 36.594 | 51.7626 | 66.6774 | 34.6433 | 12.6548 | 13.91 | 44.329
Driest 10% | 62.0774 | 126.95 | 296.471 | 110.2533 | 39.1613 | 24.8133 | 20.3677 | 40.0484 | 19.3183 | 9.7065 | 9.4967 | 23.5226
Driest 5% | 47.8 | 115.5682 | 247.7548 | 91.7533 | 25.5613 | 20.7453 | 18.6232 | 21.2984 | 13.6325 | 9.1758 | 8.48 | 16.8065
Minimum | 28.129 | 54.0714 | 78.0645 | 31.4 | 8.6355 | 7.56 | 14.4645 | 10.6452 | 4.68 | 4.7645 | 5.78 | 10.429
Yr2007 | 619.3226 | 734 | 288.6129 | 31.4 | 8.6355 | 8.5767 | 47.071 | 16.6774 | 13.4267 | 23.171 | 10.4667 | 46.8065
Yr2011 | 77.7097 | 263.7857 | 226.5161 | 444.9333 | 16.0032 | 7.56 | 18.6194 | 15.8903 | 7.8867 | 17.7774 | 9.7933 | 14.8516
Yr2015 | 1685.6774 | 1155 | 929.0968 | 674.3667 | 154.2581 | 152.1333 | 74.2903 | 22.4839 | 15.2633 | 11.1 | 54.6241 | 158.1667
Back to Map

## Slide 49
Chart: Gage #29, USGS #02319000, Suwanee Basin, WITHLACOOCHEE RIVER NEAR PINETTA, FL
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 1335.5484 | 2989.6429 | 2909.5161 | 1920.1333 | 795.2258 | 514.5 | 601.5484 | 629.5484 | 369.5667 | 265.871 | 210.3333 | 349.2581
Driest 20% | 329.9032 | 891.7143 | 1249.3871 | 758.7333 | 272.7742 | 209.5667 | 225.9355 | 237.6452 | 178.7333 | 155.129 | 133.9 | 147.6129
Driest 10% | 210.9677 | 467.3214 | 851.2903 | 443.1667 | 230.1613 | 163.5667 | 161.7097 | 157.6129 | 142.5667 | 114.0645 | 107.4667 | 132.0645
Driest 5% | 149.3871 | 260.3448 | 780.2258 | 362.5667 | 199.0323 | 150.2667 | 124.9355 | 126.0323 | 110.9333 | 107.3226 | 98.2 | 109.9355
Minimum | 115.8387 | 135.1724 | 238.2258 | 171.7 | 105.5484 | 109.9 | 88.3226 | 89.7097 | 96.5333 | 85.7419 | 78.0667 | 92.4194
Yr2007 | 1042.4839 | 1773.75 | 992.9032 | 171.7 | 105.5484 | 115.0333 | 89.6452 | 126.0323 | 142.5667 | 113.3548 | 104.0667 | 142.3871
Yr2011 | 221.1613 | 769.1429 | 690.0323 | 1150.1667 | 175.1613 | 109.9 | 333.1613 | 223.3226 | 99.1 | 128.129 | 96.6333 | 109.9355
Yr2015 | 6670 | 3638.9655 | 3581.6129 | 1770.0667 | 861.0645 | 304.8333 | 267.1613 | 274.3548 | 305.6333 | 259.6774 | 463.2667 | 702.3333
Back to Map

## Slide 50
Chart: Gage #30, USGS #02317500, Suwanee Basin, Alapaha River at Statenville, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 829.9355 | 1791.0714 | 1901.6129 | 1424.6667 | 528.9677 | 285.0667 | 312.7097 | 359.2419 | 225.0833 | 142.7097 | 88.7 | 203.2419
Driest 20% | 233.4194 | 515.6 | 836.5355 | 532.5333 | 135.1484 | 87.4733 | 96.6581 | 100.4194 | 85.2667 | 56.8387 | 45.8333 | 71.6129
Driest 10% | 86.8065 | 275.702 | 601.2129 | 386.6533 | 96.5613 | 55.4467 | 53.3613 | 65.6613 | 51.4833 | 42.2903 | 37.3333 | 43.2419
Driest 5% | 61.6065 | 178.2857 | 531.9613 | 203.4267 | 87.4516 | 48.5267 | 42.9935 | 45.5242 | 41.8083 | 36.0242 | 33.675 | 36.7339
Minimum | 35.8387 | 65.8571 | 129 | 94.8667 | 51.8387 | 29.6 | 32.0645 | 28.6774 | 25.6333 | 21.5161 | 20.9667 | 33.2581
Yr2007 | 352.9355 | 1206.8571 | 651.3226 | 94.8667 | 94.5484 | 42.1 | 32.0645 | 45.0968 | 65.3667 | 42.871 | 33.6333 | 71.6129
Yr2011 | 73.7097 | 503.2143 | 522.8387 | 626.1 | 83.5484 | 29.6 | 178.2581 | 72.7742 | 32.1333 | 56.9032 | 67.9667 | 89.0968
Yr2015 | 3576.129 | 2484.4828 | 2352.5806 | 1149.3 | 811.4839 | 173.7 | 205.871 | 204.4516 | 298.7667 | 122.4516 | 437.8667 | 932.1
Back to Map

## Slide 51
Chart: Gage #31, USGS #02314500, Suwanee Basin, SUWANNEE RIVER AT US 441, AT FARGO, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 454.8387 | 990.6552 | 1210.1452 | 906.1 | 324.8387 | 156.6 | 397.9032 | 551.6774 | 536.1333 | 346.7419 | 189.1667 | 239.2258
Driest 20% | 89.929 | 173.6978 | 345.8323 | 212.6 | 73.5484 | 35.3 | 69.4194 | 91.8387 | 99.3 | 58.5161 | 39 | 39.5806
Driest 10% | 47.0226 | 85.5821 | 153.1548 | 103.9 | 26.9355 | 17.8433 | 29.2903 | 34.5097 | 31.7 | 16.0323 | 11.8467 | 14.5161
Driest 5% | 8.0242 | 60.0482 | 97.4032 | 72.6667 | 15.7871 | 13.0667 | 25.0645 | 15.8903 | 14.1667 | 6.1387 | 3.9267 | 4.9968
Minimum | 3.0355 | 4.2821 | 6.0968 | 12.7333 | 1.8955 | 0.27565 | 1.8161 | 0.2 | 0.75882 | 0.38 | 0.12333 | 0.1
Y2007 | 34.1935 | 86 | 62.9355 | 17.0267 | 1.8955 | 15.4083 | 27.2258 | 191.6129 | 126.4333 | 533.6774 | 355.6333 | 169.7419
Y2011 | 8.0548 | 40.6071 | 30.871 | 49.6867 | 2.8097 | 0.27565 | 10.0855 | 13.3935 | 4.5327 | 6.1387 | 11.8467 | 16.8387
Y2015 | 1522.5806 | 2420 | 1997.0968 | 895.0333 | 250.5161 | 81.4 | 277.6129 | 534.1935 | 1229.4333 | 511.8387 | 195.5 | 124.7667
Back to Map

## Slide 52
Chart: Gage #32, USGS #02226500, Satilla Basin, Satilla River near Waycross, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 801.4194 | 1840.0357 | 1791.7097 | 1008.6667 | 333.3387 | 204.6167 | 363.2419 | 369.5968 | 275.5167 | 149.7258 | 91.25 | 269.6935
Driest 20% | 195.1742 | 374.3429 | 585.129 | 377.92 | 67.1226 | 52 | 56.3387 | 112.0129 | 75.0133 | 40.9032 | 30.4133 | 40.7355
Driest 10% | 86.0581 | 159.2182 | 318.2161 | 126.74 | 38.1606 | 29.699 | 22.8403 | 48.9806 | 47.3833 | 27.6226 | 22.8067 | 33.5323
Driest 5% | 54.0452 | 100.7882 | 256.4145 | 99.2683 | 25.2484 | 24.0583 | 17.3435 | 34.9829 | 29.7483 | 18.2774 | 15.3683 | 24.871
Minimum | 27.7742 | 66 | 91.0645 | 34.1333 | 11.8516 | 11.4567 | 10.071 | 12.2323 | 7.3367 | 7.5161 | 6.52 | 15.5516
Yr2007 | 32.5484 | 158.8214 | 256.3871 | 34.1333 | 11.8516 | 29.09 | 23.0581 | 24.5613 | 207.4 | 263.4194 | 43.5 | 77.0323
Yr2011 | 71.2903 | 390.8571 | 256.4194 | 371.8667 | 22.4516 | 14.6233 | 62.1742 | 49.0968 | 64.5333 | 123.2903 | 36.9 | 34.2581
Yr2015 | 2718.7097 | 1817.2414 | 2100.129 | 1305.3333 | 387.8387 | 291.9333 | 235.0323 | 371.871 | 524.4333 | 315 | 466.8667 | 455.9667
Back to Map

## Slide 53
Chart: Gage #33, USGS #02227500, Satilla Basin, LITTLE SATILLA RIVER NEAR OFFERMAN, GA
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 465.1452 | 963.4464 | 759.9355 | 404.7333 | 119.0645 | 114.9233 | 148.6129 | 233.3 | 114.89 | 90.8823 | 44.6667 | 163.2258
Driest 20% | 149.4323 | 256.0357 | 263.6839 | 121.242 | 14.7761 | 5.0409 | 17.9674 | 19.9715 | 21.8137 | 10.0883 | 5.3253 | 28.8839
Driest 10% | 94.5484 | 119.5493 | 176.8 | 41.36 | 1.32 | 1.7827 | 1.5396 | 2.9226 | 3.331 | 0.87871 | 2.0897 | 15.5455
Driest 5% | 20.7151 | 81.1536 | 133.9097 | 22.1711 | 1.1225 | 0.99167 | 0.40155 | 0.76103 | 1.0462 | 0.44174 | 0.68273 | 8.9776
Minimum | 10.1903 | 15.7321 | 53.3548 | 4.2767 | 0.3029 | 0.39267 | 0.083448 | 0.23097 | 0.077727 | 0.086667 | 0.15033 | 0.3871
Yr2007 | 94.2903 | 259.6071 | 154.8065 | 4.2767 | 1.0026 | 10.449 | 4.5 | 88.8968 | 881.7667 | 665.4194 | 38.6 | 226.871
Yr2011 | 10.1903 | 106.5679 | 108.5161 | 159.82 | 1.3213 | 4.777 | 75.5786 | 57.3171 | 24.442 | 57.3871 | 12.6633 | 21.6452
Yr2015 | 1402.3226 | 980.2759 | 1236.9677 | 1297.3 | 476.3248 | 324.97 | 5.951 | 15.4032 | 24.8887 | 2.629 | 29.47 | 85.9233
Back to Map

## Slide 54
Chart: Gage #34, USGS #02231000, St Mary Basin, ST. MARYS RIVER NEAR MACCLENNY, FL
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Driest 50% | 338.5 | 507.2869 | 550.871 | 306.5 | 76.2581 | 109.5333 | 429.8387 | 694.4516 | 546.2667 | 239.1935 | 116.6667 | 164.1935
Driest 20% | 86.3935 | 165.8286 | 165.3548 | 96.2667 | 40.5806 | 52.1 | 107.3226 | 172.8387 | 172.4667 | 64.871 | 50 | 52.3871
Driest 10% | 68.729 | 86.1464 | 100.7419 | 56.7667 | 26 | 32.3333 | 52.4516 | 81.9355 | 83.0667 | 46.0645 | 29.9 | 36.5806
Driest 5% | 47.9145 | 51.4393 | 76.8387 | 42.4667 | 24.4516 | 27.2667 | 36.6129 | 51.2581 | 71.8667 | 36.3226 | 24.7333 | 31.4194
Minimum | 38.6774 | 32.6071 | 43.2903 | 28.2667 | 12.9226 | 17.0333 | 31.2581 | 24.871 | 21.4333 | 17.2258 | 15.8 | 18.3871
Yr2007 | 90.4194 | 170.8929 | 92.0968 | 28.2667 | 12.9226 | 50.8567 | 61.2258 | 912.2903 | 301.9 | 744.2581 | 191.9667 | 94.6452
Yr2011 | 76.2903 | 485.6429 | 100.7419 | 72.4 | 26.0968 | 17.0333 | 31.9032 | 40.0968 | 32 | 55.3548 | 38.4667 | 46.2258
Yr2015 | 804.9032 | 904.0345 | 461.8387 | 502.0667 | 121.129 | 46.0333 | 98.0645 | 742.6774 | 1111.8 | 211.0645 | 76.5 | 59.0667
Back to Map

## Slide 55: Groundwater Levels
Data Source: USGS

## Slide 56: Short Term (Daily) Conditions of All Available USGS Monitoring Wells in Georgia as of January 2016

## Slide 57: Rationale for Choosing USGS Monitoring Wells
EPD monitors 15 groundwater USGS monitoring wells shown on the following slide to assess drought conditions. These wells were selected for monitoring because they have:
Long-term monitoring records consisting of three decades or more of data; and
Real-time monitoring that represents the most up-to-date conditions.

## Slide 58
10
11
12
14
15
13
USGS Wells Monitored by EPD to Assess Drought Conditions
  Flint Basin
  1. 11AA01
  2. 09M007
  3. 13L180
  4. 12M017
  5. 08K001
  6. 11K003
  7. 12K014
  8. 13J004
  9. 08G001
  10. 10G313
  11. 09F520
  Oconee Basin
  12. 21T001
  Altamaha Basin
  13. 26R001
  Savannah Basin
  14. 30AA04
  Suwanee Basin
  15. 19E009
1
3
4
5
6
7
8
9
2

## Slide 59: Groundwater Level Graphs
For each of the 15 groundwater wells, EPD has prepared a graph that shows monthly average groundwater levels from January 1, 2015 through December 31, 2015;
To help put these levels into perspective, for comparison purposes, each graph also shows:
  Monthly average levels at that same well for the years 2007 and 2011 when groundwater levels were at or near recorded low levels across much of the state; and
  And a statistical composite of historical conditions at that same gage showing the “lowest” 50, 20, 10, and 5 percent of all recorded monthly average levels at the same well.

## Slide 60: How to Read the Groundwater Level Graphs Example: Well #11, 09F520, Flint River Basin
The groundwater level graph for Well #11, USGS 09F520 shows:
  The average monthly groundwater level for May 2015 was 47ft below land surface. The statistical composite of all historical data for this well shows that monthly average groundwater levels in May have historically been lower than May 2015 about 50% of the time; about 50% of the time in May they have been higher.
  The average monthly groundwater level in May 2011 was 52ft below land surface. The statistical composite of all historical data for this well shows that average monthly groundwater elevation levels for May have historically been lower than May 2011 only 10% of the time; 90% of the time in May they have been higher.
  The average monthly groundwater level in May 2007 was 53ft below land surface. The statistical composite of all historical data for this well shows that average monthly groundwater levels for May have historically been lower than May 2007 only 5% of the time; 95% of the time in May it has been higher.
  The lowest recorded average monthly groundwater level for May was 53ft below land surface.

## Slide 61
Back to Map

## Slide 62
Back to Map

## Slide 63
Back to Map
Notes: 30AA004

## Slide 64
Back to Map

## Slide 65
Back to Map

## Slide 66
Back to Map

## Slide 67
Back to Map

## Slide 68
Back to Map

## Slide 69
Back to Map

## Slide 70
Back to Map

## Slide 71
Back to Map
Back to Interpretation

## Slide 72
Back to Map

## Slide 73
Back to Map

## Slide 74
Back to Map
Notes: 30AA004

## Slide 75
Back to Map

## Slide 76: Reservoir Levels
Data Source:
US Army Corps of Engineers

## Slide 77
6
1
2
4
5
3
7
Coosa Basin
1. Carters
2. Allatoona
Chattahoochee Basin
3. Lanier
4. West Point
5. W.F. George
Savannah Basin
6. Hartwell
7. Thurmond
EPD monitors the water levels of seven reservoirs to assess drought conditions.

## Slide 78: Reservoir Elevation Graphs
The following graphs show the reservoir elevation curves for January 1, 2015 through December 31, 2015.
Each graph also shows the Action Zone Divides (or Levels) for each reservoir
  Zone 1 is the top layer of the conservation pool
  Zone 2 is the layer below Zone 1
  Zone 4 is the lowest layer in the conservation pool
  There is no conservation storage below the bottom of Zone 4
To put 2015 reservoir elevations into perspective, elevations for 2007 and 2011 are also shown.

## Slide 79
Back to Map

## Slide 80
Back to Map

## Slide 81
Back to Map
Zone 1
Zone 2
Zone 3
Zone 4

## Slide 82
Back to Map
Zone 3
Zone 1
Zone 2
Zone 4

## Slide 83
Back to Map
Zone 1
Zone 2
Zone 3
Zone 4

## Slide 84
Back to Map
Level 1
Level 2
Level 3
Level 4

## Slide 85
Back to Map
Level 1
Level 2
Level 3
Level 4

## Slide 86: Climate Prediction Center 3-monthTemperature and Precipitation Probability Outlook and Seasonal Drought Outlook
Data Source:
http://www.cpc.ncep.noaa.gov/

## Slide 87: Temperature Outlook
The Climate Prediction Center 3-month temperature probability outlook for February – April 2016 calls for a 33% chance of below normal temperatures in extreme south Georgia with an equal chance of above or below normal temperatures throughout the rest of the state.

## Slide 88: Precipitation Outlook
For February - April 2016, there is an equal chance of above or below normal precipitation in extreme northwest Georgia while the rest of the state has a 33%-50% probability of above normal precipitation as you move from northwest to southeast across the state, with the highest probability of above normal precipitation occurring along the coast.