## Slide 1
Demonstrating Progress Toward Improving Water Supply Efficiency
Tim Cash, Bill Frechette, Johanna Smith, Wei Zeng Georgia Environmental Protection Division
Version 1.0
May 2019

## Slide 2: Presentation Outline
What is Water Loss?
How do we Track It?
Why Track Water Loss?
Water Loss Tracking Requirements in Georgia
Where We Are – The Present
Permit Renewals & Modifications – The Future
Demonstration of Progress
Resources
Notes: Brian

## Slide 3: What is water loss?
    The difference between the volume of water supplied and the volume of water billed to customers
    Expressed as “Non-Revenue Water” (Use this term instead of “Unaccounted-for-Water”)
Water Supplied
Billed Consumption
Non-Revenue Water
Notes: Brian

## Slide 4: Tracking Water Loss
AWWA M36 Methodology
Industry Best Practice since 2003
All water is “Accounted For”
Standard Definitions and Procedures
Georgia Requirement began in 2011
Notes: Brian

## Slide 5: AWWA M36 Water Balance
Real
Losses
Apparent
Losses
Unbilled
Authorized
Consumption
Billed
Authorized
Consumption
Non-
Revenue
Water
Revenue
Water
Leakage & Overflows at Storage
Billed Unmetered Consumption
Billed Metered Consumption
Billed Water Exported
Leakage on Service Lines
Leakage on Mains
Systematic Data Handling Errors
Customer Metering Inaccuracies
Unauthorized Consumption
Unbilled Unmetered Consumption
Unbilled Metered Consumption
Water
Imported
Own
Sources
Total
System
Input
( allow
for
known
errors )
Water
Losses
Authorized
Consumption
Water
Exported
Water
Supplied
Notes: Brian

## Slide 6: Real Losses
Also called Physical Losses – Water that enters the distribution system, but never reaches a user
Examples Include:
      Leakage on transmission and distribution mains
      Storage tank overflows
      Service Line leakage up to customer meter
Reducing real losses extends the water resource
Leak on Grand Avenue in Oakland, CA (April 11, 2008)
https://www.sfgate.com/bayarea/article/Oakland-Leaking-water-main-on-Grand-Avenue-3220180.php
Notes: Brian

## Slide 7: Apparent Losses
Also called Paper or Economic Losses – Water that reaches a user, but is not properly measured or paid for
      Theft
      Customer metering inaccuracies
      Data handling errors
Reducing Apparent losses does not create any new water, but increases utility revenue
Associated values may be different than those of Real Losses
https://www.townofclaytonnc.org/Public-Works/water-sewer.aspx
Blazing the Path – Georgia’s Water Loss Control Program, 2018
Notes: Brian

## Slide 8: Why track water loss?
Reduction in water utility operating costs
    Address Real Losses to reduce production costs
    Address Apparent Losses to reduce water produced but not billed
Fits into the big picture of water conservation and water efficiency, which demonstrates responsible water stewardship
EPD permits water withdrawals based on demonstrated need and reasonable use
Water Efficiency
Demand Side Conservation
Supply Side Conservation
Customer Behavior
Technology
Leakage Reduction
Metering Accuracy
Water Loss Assessment and Control is here
Notes: Brian

## Slide 9: Tracking water loss in georgia
Originated with the Water Stewardship Act (WSA) enacted by 2010 Georgia General Assembly
Recognizes imminent needs to:
      Create a culture of water conservation in the State of Georgia
      Plan for water supply enhancement during future extreme drought conditions and water emergencies
https://atlantaregional.org/natural-resources/water-wars/tri-state-water-wars-background-and-history/
Notes: Johanna

## Slide 10: Rules for Public Water Systems to Improve Water Supply Efficiency
    Georgia Rule 391-3-33 enacted to implement WSA
    Applies to:
      Systems serving >3,300 individuals
      All permit renewals and modifications to increase permitted water withdrawal limits
    Requirements Include:
      Conduct Annual Water Loss Audits (due March 1)
      Development of Water Loss Control Program (as of July 2016)
      Development of individual goals to set measures of water supply efficiency (defined by water system)
      Demonstration of progress toward improving water supply efficiency
Notes: *Go through quickly, more detail later in the slides

## Slide 11: The Present
7 Years of Validated Water Audits Online (https://epd.georgia.gov/water-loss-audit-results)
Georgia Water Loss Control Manual Version 2.0 (3rd edition – Green Cover)
New water withdrawal applications now under development to help with submission of relevant information
Outreach and Guidance for Demonstrating Progress in Improving Water Efficiency under development
Notes: Johanna

## Slide 12: Permit renewals & modifications The Future
Reminder, the Rules for Public Water Systems to Improve Water Supply Efficiency require the following:
  Conduct Annual Water Loss Audits (due March 1)
  Development of Water Loss Control Program (as of July 2016)
  Development of individual goals to set measures of water supply efficiency
  Demonstration of progress toward improving water supply efficiency
Notes: Johanna

## Slide 13: Water loss control program
  EPD will begin asking for submission as part of permit application package
  If you don’t yet have one, submission may be required in the permit
  Must include goals and timelines, which may become enforceable through permit. May include:
    Infrastructure Leakage Index (ILI)
    Data Validity Score (DV)
    Apparent Losses
    Real Losses
    Economic Level of Leakage (ELOL)
  May consider other applicable goals (i.e. Metro District Water Loss Targets)
Reference: Water Audits and Water Loss Control for Public Water Systems, Environmental Protection Agency (EPA)

## Slide 14: Permit renewals & modifications The Future
Reminder, the Rules for Public Water Systems to Improve Water Supply Efficiency require the following:
  Conduct Annual Water Loss Audits (due March 1)
  Development of Water Loss Control Program (as of July 2016)
  Development of individual goals to set measures of water supply efficiency
  Demonstration of progress toward improving water supply efficiency
Notes: Johanna

## Slide 15: Demonstration of progress
What is Progress? (from Rule 391-3-33)
    Improvement of Data Validity Score (DV)
    Development and implementation of a Water Loss Control Program
    Improvement in performance measures once a reliable DV score has been achieved
      Apparent Losses
      Real Losses
    Economic Level of Leakage has been achieved and maintained
How does EPD evaluate it?
    Data trends and comments available from past Water Audits
    EPD may request a narrative explaining variability and any programs or measures you have implemented to reduce water loss
    If a narrative cannot be produced that explains progress, conditions may be included in the permit to help accomplish it

## Slide 16: How do we recognize progress?
Example 1
    Sharp decrease in Real Losses / Connection / Day
    Consistent increase in DV
Chart: Real Loss / Connection / Day
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Real Loss/Conn/Day | 49.2952 | 24.4461 | 32.2588 | 31.5 | 23.2388 | 17.2628
Chart: Data Validity
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
DV | 60.4225 | 75.4035 | 69.7018 | 73 | 74.2511 | 73.8862
Real Loss = 65% decrease (2012 – 2017)
DV = 22% increase (2012 – 2017)

## Slide 17: How do we recognize progress?
Example 2
    Consistent decrease in Real Losses / Connection / Day
    Sharp increase in DV
Chart: Real Loss / Connection / Day
Chart: Real Loss / Conn / Day
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Real Loss/Conn/Day | 99.28 | 136.89 | 113.19 | 94.94 | 87.97 | 78.72
Chart: Data Validity Score
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
DV | 40.9589 | 59.8765 | 61.8839 | 66 | 70.3185 | 70.3945
DV = 72% increase (2012 – 2017)
Real Loss = 20% decrease (2012 – 2017)

## Slide 18: How do we recognize progress?
Example 3
    Sharp decrease in Real Losses / Connection / Day
    Sharp & stable increase in DV
Chart: Real Loss / Connection / Day
DV = 54% increase (2012 – 2017);
DV = 3% decrease (2014 – 2017)
Real Loss = 78% decrease (2012 – 2017)
Chart: Real Loss / Connection / Day
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Real Loss / Conn / Day | 69.765 | 40.106 | 27.1823 | 21.76 | 21.7015 | 15.2471
Chart: Data Validity
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017
DV | 43.3333 | 56.7816 | 69.3261 | 67 | 67.4533 | 67.0374

## Slide 19: How do we recognize progress?
Example 4
    Consistent decrease in Real Losses / Length of Main / Day
    Consistent increase in DV
Chart: Real Loss / Connection / Day
DV = 18% increase (2011 – 2017)
Real Loss = 56% decrease (2011 – 2017)
Chart: Real Loss / Length of Main / Day
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Real Loss / Length of Main / Day | 880.4052 | 500.5057 | 675.3239 | 609.8499 | 386.805 | 491.8597 | 383.4627
Chart: Data Validity
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
DV | 66.9474 | 67.1579 | 69.2632 | 77.0093 | 77 | 78.0983 | 79.4877

## Slide 20: How do we recognize progress?
Example 5
    Consistent increase in Real Loss / Connection / Day
    Sharp increase in DV
Chart: Real Loss / Connection / Day
DV = 18% increase (2011 – 2017)
Real Loss = 192% increase (2011 – 2017)
Chart: Real Loss / Connection / Day
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Real Loss / Conn / Day | 28.4412 | 67.3063 | 78.7721 | 62.6671 | 54.45 | 70.7996 | 82.9476
Chart: Data Validity
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
 | 68.2278 | 69.8592 | 69.6552 | 71.9059 | 80 | 80.4251 | 80.4364

## Slide 21: How do we recognize progress?
Example 6
    Variable Real Loss / Connection / Day
    Sharp increase in DV
Chart: Real Loss / Connection / Day
DV = 36% increase (2011 – 2017)
Real Loss = 19% increase (2011 – 2017)
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
DV | 60.8235 | 74.1176 | 75.0588 | 82.0377 | 82 | 78.8004 | 82.5285
Chart: Real Loss / Connection / Day
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
% Loss | 24.0564 | 30.3467 | 22.5773 | 21.3502 | 39.78 | 19.3521 | 28.5943

## Slide 22: resources
Georgia Water Loss Control Manual
http://epd.georgia.gov/sites/epd.georgia.gov/files/related_files/site_page/GA%20Water%20Loss%20Manual%20V2.0_Final_3-15-18%20Update.pdf
American Water Works Association Water Loss Control Resources
https://www.awwa.org/Resources-Tools/Resources/Water-Loss-Control
Water Research Foundation Leakage Component Analysis Tools
http://www.waterrf.org/Pages/Projects.aspx?PID=4372
Georgia Association of Water Professionals (GAWP) Water Loss Auditing Guidance
https://gawp.site-ym.com/page/WaterLossAudits
Georgia Rural Water Association (GRWA) Water Loss Technical Assistance Program
http://www.grwa.org/news.cfm?id=6146
Water Audits and Water Loss Control for Public Water Systems (EPA)
https://www.epa.gov/sites/production/files/2015-04/documents/epa816f13002.pdf
Notes: Johanna

## Slide 23: resources
GAWP Advanced Water Loss Control Workshop
May 21, 2019, 10:00 AM – 3:30 PM
GAWP Headquarters – Greene Room
    Interpreting Audits Results / Next Steps
    Understanding Components of Real and Apparent Losses
    Tools Available
    Leakage Component Analysis (LCA) Model
    Data Needed for LCA Tool
    Utility Case Studies
  Register by May 19, 2019
Notes: Johanna

## Slide 24: Questions?
Johanna Smith
    Surface Water Unit Manager
    Water Supply Program
    Phone: 404-656-6937
    Email: Johanna.Smith@dnr.ga.gov
Wei Zeng
    Water Supply Program Manager
    Phone: 404-463-2883
    Email: Wei.Zeng@dnr.ga.gov
Bill Frechette
    Groundwater Unit Manager
    Water Supply Program
    Phone: 404-656-6937
    Email: Bill.Frechette@dnr.ga.gov
Tim Cash
    Water Supply Program
    Phone: 404-463-3948
    Email: Tim.Cash@dnr.ga.gov