STATE OF GEORGIA

DEPARTMENT OF NATURAL RESOURCES

ENVIRONMENTAL PROTECTION DIVISION

FACT SHEET

NATIONAL POLLUTANT DISCHARGE ELIMINATION SYSTEM

GENERAL PERMIT NO. GAG550000

TREATED WASTEWATER DISCHARGES

ASSOCIATED WITH PRIVATE AND INSTITUTIONAL DEVELOPMENT

WATER POLLUTION CONTROL PLANT ACTIVITIES

The 1972 amendments to the Federal Water Pollution Control Act  (also referred to as the Clean Water Act or CWA) prohibit the discharge of any pollutant to waters of the United States from a point source unless the discharge is authorized by a National Pollutant Discharge Elimination System (NPDES) permit.  Efforts to improve water quality under the NPDES program are focused on reducing pollutants in discharges of treated wastewater including discharges from private and institutional development (PID) facilities, which are built to serve nonmunicipal domestic sewage.

The reissuance of General Permit No. GAG550000 authorizes treated wastewater discharges to the waters of the State of Georgia from PIDs that are presently covered by the current general PID permit.  Coverage under the general permit can also be obtained by those PID WPCP’s covered under an individual NPDES permit that meet the criteria for general PID permit coverage. No new facilities will be covered under this permit. The general PID permit will not result in any increased loadings or less stringent conditions or limitations for any facility covered under this permit. Coverage under this permit is initiated by submitting a Notice of Intent (NOI). The NOI includes basic information about the facility and the specific waters of Georgia where the discharges occur.  Coverage under this permit can be terminated by submitting a Notice of Termination (NOT).  An NOT shall be submitted if discharges from the permitted facility cease or a new permittee takes over facility operations. Once a completed NOI or NOT is received, EPD will notify the applicant in writing whether they have received coverage under the general PID permit or whether coverage has been terminated. NOI and NOT forms are available on EPD’s website at http://epd.georgia.gov.

LIMITATIONS AND MONITORING REQUIREMENTS

The general PID permit provides coverage only for privately owned or institutional systems that operate as a pond system, mechanical system, or septic tank/sand filter system at low or high design flows.  Facilities with design flows less than 10,000 gallons per day or 0.010 million gallons per day (MGD) will be in the “small” (low flow) category and facilities with design flows greater than or equal to 0.010 MGD up to 0.075 MGD will be in the “large” (high flow) category.  Facilities with design flows between 0.075 MGD and 0.50 MGD may receive coverage under the large category on a case by case basis.  Any facility that has a design flow higher than 0.50 MGD will not receive coverage under the general PID permit, but may be permitted under an individual NPDES permit.  The effluent limitations and monitoring requirements are specific for treatment type and design flow.

The pond systems consist of waste stabilization ponds or multi-stage pond systems and operate at low or high design flows.  Mechanical systems consist of either activated sludge treatment, trickling filters, sequencing batch reactors, combination pond and mechanical systems, septic tank-sand filter systems, or any mechanical system approved as such by EPD and operate at the flow ranges described above.  Facilities eligible for coverage under GAG550000 include, but are not limited to, mobile home parks, campgrounds/camps, City or County owned schools, City or County owned prisons, churches, nursing homes and motels.

The NOI requires the permittee to submit information on the design flow.  This information along with the flow limitation and other design information will be used to determine the flow capacity of each facility.  The specific effluent limitations will depend on the facility design flow and type of treatment.

The limitations for BOD and TSS in this permit comply with technology based secondary treatment standards and apply the Best Conventional Pollutant Control Technology (BCT) for systems designed to treat domestic only wastewater. The permit includes effluent limitations that are specific to facility design (whether it is a pond type system or mechanical system).  The permit also includes water quality based effluent limitations for Fecal Coliform Bacteria and pH.  An effluent limitation and two-year compliance schedule have been included in the permit for total residual chlorine. The total residual chlorine limit is 0.011 mg/L and is a daily max.

The following monitoring requirements and effluent limitations apply to the different facility types in this permit.

MECHANICAL TREATMENT PLANTS

(Large – Reference footnotes 1 and 3)

(Small – Reference footnotes 2 and 4)

Table 1 - Mechanical Treatment Plants BOD, TSS, and Fecal Coliform Limitations

| Parameters | Discharge limitations in mg/L (kg/day) unless otherwise specified | Monitoring Requirements |
| --- | --- | --- |
|  | Monthly Average | Weekly Average | Measurement Frequency1,2 | Sample Type3,4 | Sample Location |
| Flow (MGD) | -- | -- | See Below | See Below | Effluent |
| Biochemical Oxygen Demand (5-day) | 30 | 45 | See Below | See Below | Effluent |
| Total Suspended Solids (TSS) | 30 | 45 | See Below | See Below | Effluent |
| Fecal Coliform Bacteria (#/100 mL) | 200 | 400 | See Below | Grab | Effluent |

Table 2 - Mechanical Treatment Plants pH and Total Residual Chlorine Limitations

| Parameters | Discharge limitations as specified | Monitoring Requirements |
| --- | --- | --- |
|  |  | Measurement Frequency1,2 | Sample Type | Sample Location |
| pH, Minimum – Maximum (Standard Unit) | 6.0 – 8.5 | See Notes | Grab | Effluent |
| Total Residual Chlorine5 (mg/L) | 0.011 | See Notes | Grab | Effluent |

Notes:

- Large Mechanical Treatment Plants shall be required to monitor for the specific parameters once per month.

- Small Mechanical Treatment Plants shall be required to monitor for the specific parameters  once per quarter.

- Large Mechanical Treatment Plants require continuous flow recording and shall collect composite samples for BOD and TSS.

- Small Mechanical Treatment Plants require instantaneous flow recording and shall collect grab samples for BOD and TSS.

- Total residual chlorine shall be a daily maximum limit. Total Residual Chlorine monitoring requirements only apply if chlorine is in use at the facility. Refer to Part I.C.8 of the draft permit for the compliance schedule.

POND SYSTEMS

(Large – Reference footnote 1)

(Small – Reference footnote 2)

Table 3 - Pond Systems BOD, TSS, and Fecal Coliform Limitations

| Parameters | Discharge limitations in mg/L (kg/day) unless otherwise specified | Monitoring Requirements |
| --- | --- | --- |
|  | Monthly Average | Weekly Average | Measurement Frequency1,2 | Sample Type | Sample Location |
| Flow (MGD) | -- | -- | See Notes | Instantaneous | Effluent |
| Biochemical Oxygen Demand (5-day) | 30 | 45 | See Notes | Grab | Effluent |
| Total Suspended Solids | 90 | 120 | See Notes | Grab | Effluent |
| Fecal Coliform Bacteria (#/100 mL) | 200 | 400 | See Notes | Grab | Effluent |

Table 4 - Pond Systems pH and Total Residual Chlorine Limitations

| Parameters | Discharge limitations as specified | Monitoring Requirements |
| --- | --- | --- |
|  |  | Measurement Frequency1,2 | Sample Type | Sample Location |
| pH, Minimum – Maximum (Standard Unit) | 6.0 – 8.5 | See Notes | Grab | Effluent |
| Total Residual Chlorine3 (mg/L) | 0.011 | See Notes | Grab | Effluent |

Notes:

- Large Pond Systems shall monitor at a frequency of once per month.

- Small Pond Systems shall monitor at a frequency of once per quarter.

- Total residual chlorine shall be a daily maximum limit. Total residual chlorine monitoring requirements only apply if chlorine is in use at the facility. Refer to Part I.C.8 of the draft permit for the compliance schedule.

PERMIT COVERAGE

The cover letter that notifies the applicant of coverage under the General Permit will specifically identify:

- The name and location of the facility

- The type of system

- The flow limitation

- Address of the EPD District Office responsible for receiving Discharge Monitoring Reports and tracking compliance.

Along with the cover letter notifying the applicant of coverage under the general permit, a copy of the permit will be sent to the permittee.  If the facility is currently covered under an individual NPDES permit, once EPD approves coverage under this general permit, the existing permit will be revoked in accordance with Part II.B.11 of the attached draft permit.

TRUST INDENTURE

Non-governmentally owned wastewater treatment systems should execute a trust indenture with a local government body or other trustee approved by the Division.  This trust indenture must assure continuity of operation of the facility in the event of operational or financial default by the owner.  Upon submittal of the NOI for coverage under this general permit, the permittee will be required to submit one of the following:

- Owners of systems who already have an executed trust indenture are required to submit a copy of the trust indenture along with the NOI.

- Owners of systems who do not have a trust indenture must submit a trust indenture within 180 days of the effective date of the permit.

EPD encourages the owner of the system to make every effort to enter into a trust indenture with a local governmental authority.  However, it is understood that an owner of a PID system may not be able to obtain a trust indenture from local governmental authorities and may have to enter an indenture with a private entity.

PROCEDURES FOR THE FORMULATION OF FINAL DETERMINATIONS

1.	Comment Period

EPD proposes to re-issue a NPDES general PID permit subject to the effluent limitations and special conditions outlined above.  These determinations are tentative.

Persons wishing to comment upon or object to the proposed determinations are invited to submit same in writing to the EPD address below, or via e-mail at EPD.comments@dnr.state.ga.us, within 30 days of the date of initiation of the public comment period.  All comments received prior to that date will be considered in the formulation of final determinations regarding the application.  The NPDES permit number should be placed on the top of the first page of comments to ensure that your comments will be forwarded to the appropriate staff.

Georgia Department of Natural Resources

Environmental Protection Division

Watershed Protection Branch

2 Martin Luther King, Jr. Drive, Suite 1152 East

Atlanta, Georgia 30334

2. 	Public Hearing

Any applicant, affected state or interstate agency, the Regional Administrator of the U.S. Environmental Protection Agency (EPA) or any other interested agency, person or group of persons may request a public hearing with respect to an NPDES permit application if such request is filed within thirty (30) days following the date of the public notice for such application.  Such request must indicate the interest of the party filing the request, the reasons why a hearing is requested, and those specific portions of the application or other NPDES form or information to be considered at the public hearing.  The Director shall hold a hearing if it is determined that there is sufficient public interest in holding such a hearing.  If a public hearing is held, notice of same shall be provided at least thirty (30) days in advance of the hearing date.

The permit application, draft permit, comments received and other information are available for review at the Wastewater Regulatory Program, 2 Martin Luther King Jr. Drive, Suite 1152 East, Atlanta, Georgia 30334 between the hours of 8:00 a.m. and 4:30 p.m., Monday through Friday.

In the event that a public hearing is held, both oral and written comments will be accepted; however, for the accuracy of the record, written comments are encouraged.  The Director or a designee reserves the right to fix reasonable limits on the time allowed for oral statements and such other procedural requirements, as deemed appropriate.

Following a public hearing, the Director, unless it is decided to deny the permit, may make such modifications in the terms and conditions of the proposed permit as may be appropriate and shall issue the permit.  Notice of issuance or denial will be circulated to those persons or groups who participated in the hearing; to those persons or groups who submitted written comments to the Director on the proposed permit within thirty (30) days from the date of the public notice of the application for permit; and to all persons or groups included on the EPD mailing list.

3. 	Contested Hearings

Any person who is aggrieved or adversely affected by the issuance or denial of a permit by the Director of EPD may petition the Director for a hearing if such petition is filed in the office of the Director within thirty (30) days from the date of notice of such permit issuance or denial.  Such hearing shall be held in accordance with the EPD Rules, Water Quality Control, subparagraph 391-3-6-.01.

Petitions for a contested hearing must include the following:

1.	The name and address of the petitioner;

2.	The grounds under which petitioner alleges to be aggrieved or adversely affected by the issuance or denial of a permit;

3.	The reason or reasons why petitioner takes issue with the action of the Director;

4.	All other matters asserted by petitioner which are relevant to the action in question.

4. 	Issuance of the Permit When No Public Hearing is Held

If no public hearing is held, and, after review of the written comments received, the Director determines that a permit should be issued and that the determinations as set forth in the proposed permit are substantially unchanged, the permit will be issued and will become final in the absence of a request for a contested hearing.  Notice of issuance or denial will be circulated to those persons who submitted written comments to the Director on the proposed permit within thirty (30) days from the date of the public notice of such proposed permit; and to all persons or groups included on the EPD mailing list.

If no public hearing is held, but the Director determines, after a review of the written comments received, that a permit should be issued but that substantial changes in the proposed permit are warranted, public notice of the revised determinations will be given and written comments accepted in the same manner as the initial notice of application was given and written comments accepted pursuant to EPD Rules, Water Quality Control, subparagraph 391-3-6-.06(7)(b).  The Director shall provide an opportunity for public hearing on the revised determinations.  Such opportunity for public hearing and the issuance or denial of a permit thereafter shall be in accordance with the procedures as are set forth above.